® / 34-36 Peyo Yavorov blvd, / Sofia 1164, Bulgaria	tel +359 2 423 4455 / proektsoft.bg@gmail.com / https://calcpad.eu

A CALCPAD PROGRAM
FOR ANALYSIS OF PLANE FRAMES
WITH VARIABLE CROSS-SECTIONS

─◊─◊──◊───◊────⧫────◊───◊──◊─◊─

(using the finite element method)

by

Eng. Nedelcho Ganchovsky
Table of contents
# Introduction
This Calcpad program performs analysis of plane frames with variable cross-sections using the finite element method. The input data is entered in text format as vectors and matrices as follows:
- joint coordinates;
- joint numbers at the ends of the elements;
- material properties;
- dimensions and types of cross-sections;
- support conditions;
- load values.
As a result, diagrams of internal forces and deflections of structural elements are obtained. The schemes are automatically generated by the program, using the SVG graphical format.
# Calcpad source code
1 / 2 / 3 / 4 / 5 / 6 / 7 / 8 / 9 / 10 / 11 / 12 / 13 / 14 / 15 / 16 / 17 / 18 / 19 / 20 / 21 / 22 / 23 / 24 / 25 / 26 / 27 / 28 / 29 / 30 / 31 / 32 / 33 / 34 / 35 / 36 / 37 / 38 / 39 / 40 / 41 / 42 / 43 / 44 / 45 / 46 / 47 / 48 / 49 / 50 / 51 / 52 / 53 / 54 / 55 / 56 / 57 / 58 / 59 / 60 / 61 / 62 / 63 / 64 / 65 / 66 / 67 / 68 / 69 / 70 / 71 / 72 / 73 / 74 / 75 / 76 / 77 / 78 / 79 / 80 / 81 / 82 / 83 / 84 / 85 / 86 / 87 / 88 / 89 / 90 / 91 / 92 / 93 / 94 / 95 / 96 / 97 / 98 / 99 / 100 / 101 / 102 / 103 / 104 / 105 / 106 / 107 / 108 / 109 / 110 / 111 / 112 / 113 / 114 / 115 / 116 / 117 / 118 / 119 / 120 / 121 / 122 / 123 / 124 / 125 / 126 / 127 / 128 / 129 / 130 / 131 / 132 / 133 / 134 / 135 / 136 / 137 / 138 / 139 / 140 / 141 / 142 / 143 / 144 / 145 / 146 / 147 / 148 / 149 / 150 / 151 / 152 / 153 / 154 / 155 / 156 / 157 / 158 / 159 / 160 / 161 / 162 / 163 / 164 / 165 / 166 / 167 / 168 / 169 / 170 / 171 / 172 / 173 / 174 / 175 / 176 / 177 / 178 / 179 / 180 / 181 / 182 / 183 / 184 / 185 / 186 / 187 / 188 / 189 / 190 / 191 / 192 / 193 / 194 / 195 / 196 / 197 / 198 / 199 / 200 / 201 / 202 / 203 / 204 / 205 / 206 / 207 / 208 / 209 / 210 / 211 / 212 / 213 / 214 / 215 / 216 / 217 / 218 / 219 / 220 / 221 / 222 / 223 / 224 / 225 / 226 / 227 / 228 / 229 / 230 / 231 / 232 / 233 / 234 / 235 / 236 / 237 / 238 / 239 / 240 / 241 / 242 / 243 / 244 / 245 / 246 / 247 / 248 / 249 / 250 / 251 / 252 / 253 / 254 / 255 / 256 / 257 / 258 / 259 / 260 / 261 / 262 / 263 / 264 / 265 / 266 / 267 / 268 / 269 / 270 / 271 / 272 / 273 / 274 / 275 / 276 / 277 / 278 / 279 / 280 / 281 / 282 / 283 / 284 / 285 / 286 / 287 / 288 / 289 / 290 / 291 / 292 / 293 / 294 / 295 / 296 / 297 / 298 / 299 / 300 / 301 / 302 / 303 / 304 / 305 / 306 / 307 / 308 / 309 / 310 / 311 / 312 / 313 / 314 / 315 / 316 / 317 / 318 / 319 / 320 / 321 / 322 / 323 / 324 / 325 / 326 / 327 / 328 / 329 / 330 / 331 / 332 / 333 / 334 / 335 / 336 / 337 / 338 / 339 / 340 / 341 / 342 / 343 / 344 / 345 / 346 / 347 / 348 / 349 / 350 / 351 / 352 / 353 / 354 / 355 / 356 / 357 / 358 / 359 / 360 / 361 / 362 / 363 / 364 / 365 / 366 / 367 / 368 / 369 / 370 / 371 / 372 / 373 / 374 / 375 / 376 / 377 / 378 / 379 / 380 / 381 / 382 / 383 / 384 / 385 / 386 / 387 / 388 / 389 / 390 / 391 / 392 / 393 / 394 / 395 / 396 / 397 / 398 / 399 / 400 / 401 / 402 / 403 / 404 / 405 / 406 / 407 / 408 / 409 / 410 / 411 / 412 / 413 / 414 / 415 / 416 / 417 / 418 / 419 / 420 / 421 / 422 / 423 / 424 / 425 / 426 / 427 / 428 / 429 / 430 / 431 / 432 / 433 / 434 / 435 / 436 / 437 / 438 / 439 / 440 / 441 / 442 / 443 / 444 / 445 / 446 / 447 / 448 / 449 / 450 / 451 / 452 / 453 / 454 / 455 / 456 / 457 / 458 / 459 / 460 / 461 / 462 / 463 / 464 / 465 / 466 / 467 / 468 / 469 / 470 / 471 / 472 / 473 / 474 / 475 / 476 / 477 / 478 / 479 / 480 / 481	#include svg_drawing.cpd / "Analysis of plane frames with variable cross-sections / '<h4>Joint coordinates - xJ; yJ</h4> / #hide / #deg / δz = 10^-12 / Precision = 10^-8 / x_J = [0; 0; 8; 16; 16]*m / y_J = [0; 8; 10; 8; 0]*m / #show / x_J','y_J / n_J = len(x_J) / '<h4>Elements - [J1; J2]</h4> / #hide / e_J = [1; 2|3; 2|3; 4|5; 4] / #show / transp(e_J) / n_E = n_rows(e_J) / 'Element endpoint coordinates / x_1(e) = x_J.e_J.(e; 1)','y_1(e) = y_J.e_J.(e; 1) / x_2(e) = x_J.e_J.(e; 2)','y_2(e) = y_J.e_J.(e; 2) / 'Element length - 'l(e) = sqrt((x_2(e) - x_1(e))^2 + (y_2(e) - y_1(e))^2) / 'Element directions / c(e) = (x_2(e) - x_1(e))/l(e)','s(e) = (y_2(e) - y_1(e))/l(e) / 'Transformation matrix / 'Diagonal 3x3 block -'t(e) = [c(e); s(e); 0|-s(e); c(e); 0|0; 0; 1] / 'Generation of the full transformation matrix / T(e) = add(t(e); add(t(e); matrix(6; 6); 1; 1); 4; 4) / '<h4>Supports - [Joint; cx; cy; cr]</h4> / #hide / c = [1; 10^20kN/m; 10^20kN/m; 0kNm|5; 10^20kN/m; 10^20kN/m; 10^20kNm] / #show / c / n_c = n_rows(c) / '<h4>Loads - [Element, qx, qy]</h4> / #hide / q = [1; 10kN/m; 0kN/m|2; 0kN/m; -20kN/m|3; 0kN/m; -10kN/m] / n_q = n_rows(q) / q_x = vector(n_E)*kN/m / q_y = vector(n_E)*kN/m / $Repeat{q_x.(q.(i; 1)) = q_x.(q.(i; 1)) + q.(i; 2) @ i = 1 : n_q} / $Repeat{q_y.(q.(i; 1)) = q_y.(q.(i; 1)) + q.(i; 3) @ i = 1 : n_q} / #show / q / 'Load values on elements / q_x / q_y / '<h4>Scheme of the structure</h4> / #hide / w = max(x_J) / h = max(y_J) / W = 240 / H = h*W/w / k = W/w / #def svg$ = '<svg viewbox="'-3m*k' '-2m*k' '(w + 6m)*k' '(h + 4m)*k'" xmlns="http://www.w3.org/2000/svg" version="1.1" style="font-family: Georgia Pro; font-size:5pt; width:'W + 150'pt; height:'H + 200*H/W'pt"> / #def thin_style$ = style = "stroke:green; stroke-width:1; fill:none" / #def thick_style$ = style = "stroke:green; stroke-width:2; fill:none" / k_q = m/kN / #show / #val / svg$ / #for i = 1 : n_E / #hide / x1 = x_1(i)*k / y1 = (h - y_1(i))*k / x2 = x_2(i)*k / y2 = (h - y_2(i))*k / q_xi = q_x.i / q_yi = q_y.i / α = atan2(c(i); s(i)) / #if α ≥ 135 / α = α - 180 / #end if / #if α < -45 / α = α + 180 / #else if α < 0 / α = 360 + α / #end if / #if q_xi ≠ 0kN/m / #hide / x3 = x2 - q_xi*k_q','y3 = y2 / x4 = x1 - q_xi*k_q','y4 = y1 / x = (x3 + x4)/2 - 5*sign(q_xi) / y = (y3 + y4)/2 / #show / '<polygon points="'x1','y1' 'x2','y2' 'x3','y3' 'x4','y4'" style="stroke:magenta; stroke-width:1; stroke-opacity:0.3; fill:magenta; fill-opacity:0.1;" /> / text$(x;y;α;qx='abs(q_xi)') / #end if / #if q_yi ≠ 0kN/m / #hide / x3 = x2','y3 = y2 + q_yi*k_q / x4 = x1','y4 = y1 + q_yi*k_q / x = (x3 + x4)/2 / y = (y3 + y4)/2 + 5*sign(q_yi) / #show / '<polygon points="'x1','y1' 'x2','y2' 'x3','y3' 'x4','y4'" style="stroke:dodgerblue; stroke-width:1; stroke-opacity:0.4; fill:dodgerblue; fill-opacity:0.15;" /> / text$(x;y;α;qy='abs(q_yi)') / #end if / #show / line$(x1; y1; x2; y2; main_style$) / #loop / '<g id="frame"> / #for i = 1 : n_E / #hide / x1 = x_1(i)*k / y1 = (h - y_1(i))*k / x2 = x_2(i)*k / y2 = (h - y_2(i))*k / #show / line$(x1; y1; x2; y2; main_style$) / #loop / #for i = 1 : n_c / #hide / j = c.(i; 1) / x1 = x_J.j*k / y1 = (h - y_J.j)*k / δ = w/30*k*sign(x1 - w/2*k) / x2 = x1 - δ / y2 = y1 - abs(δ) / x3 = x1 + δ / y3 = y1 + abs(δ) / #show / #if c.(i; 2) ≠ 0kN/m / #if c.(i; 3) ≠ 0kN/m / #if c.(i; 4) ≠ 0kNm / line$(x1; y1; x1; y3; thin_style$) / line$(x2; y3; x3; y3; thick_style$) / #else / line$(x2; y3; x3; y3; thick_style$) / line$(x2; y3; x1; y1; thin_style$) / line$(x3; y3; x1; y1; thin_style$) / #end if / #else / #if c.(i; 4) ≠ 0kNm / line$(x1; y1; x2; y1; thin_style$) / line$(x2; y2; x2; y3; thick_style$) / line$(x2 - δ/2; y2; x2 - δ/2; y3; thick_style$) / #else / line$(x2; y2; x1; y1; thin_style$) / line$(x2; y3; x1; y1; thin_style$) / line$(x2; y2; x2; y3; thin_style$) / line$(x2 - δ/2; y2; x2 - δ/2; y3; thick_style$) / #end if / #end if / #else / #if c.(i; 3) ≠ 0kN/m / #if c.(i; 4) ≠ 0kNm / line$(x1; y1; x1; y3; thin_style$) / line$(x2; y3; x3; y3; thick_style$) / line$(x2; y3 + abs(δ)/2; x3; y3 + abs(δ)/2; thick_style$) / #else / line$(x2; y3; x3; y3; thin_style$) / line$(x2; y3; x1; y1; thin_style$) / line$(x3; y3; x1; y1; thin_style$) / line$(x2; y3 + abs(δ)/2; x3; y3 + abs(δ)/2; thick_style$) / #end if / #else / line$(x2; y2; x3; y3; thick_style$) / #end if / #end if / #loop / '</g> / #for i = 1 : n_E / #hide / x = (x_1(i) + x_2(i))*k/2 / y = (h - (y_1(i) + y_2(i))/2)*k / #show / texth$(x + 0.8m*sign(W/2 - x)*k; y + 0.6m*k; e'i') / #loop / #for i = 1 : n_J / point$(x_J.i*k; (h - y_J.i)*k; point_style$) / texth$((x_J.i - 0.7m*sign(w/2 - x_J.i))*k; (h - y_J.i - 0.4m)*k; J'i') / #loop / dimv$((w + 2m)*k; (h - y_J.4)*k; h*k; 'y_J.4') / dimv$((w + 2m)*k; 0; (h - y_J.4)*k; 'h - y_J.4') / dimh$(0; w*k; (h + 1.5m)*k; 'w') / '</svg> / #equ / '<h4>Materials</h4> / 'Modules of elasticity -'E = [45; 35]*GPa / 'Poisson coefficients -'ν = [0.2; 0.2] / 'Shear modules -'G = E/(2*(1 + ν)) / 'Assignments on elements -'e_M = [1; 2; 2; 1] / '<h4>Cross-sections</h4> / #hide / b = vector(2)','h = vector(2) / #show / 'Section S1 -'b_1 = 300mm','h_1 = 300mm / 'Section S2 -'b_2 = 300mm','h_2 = 900mm / 'General representation / 'Width -'b(ξ; z) = b_1 + (b_2 - b_1)*ξ / 'Height -'h(ξ) = h_1 + (h_2 - h_1)*ξ / '<h4>Cross section properties</h4> / 'Area -'A(ξ) = $Area{b(ξ; z) @ z = 0mm : h(ξ)}|cm^2 / 'First moment of area -'S(ξ) = $Area{b(ξ; z)*z @ z = 0mm : h(ξ)}|cm^3 / 'Centroid -'z_c(ξ) = S(ξ)/A(ξ)|mm / 'Second moment of area -'I(ξ) = $Area{b(ξ; z)*(z - z_c(ξ))^2 @ z = 0mm : h(ξ)}|cm^4 / 'First moment of area below z -'S_1(ξ; z) = $Area{b(ξ; ζ)*(z_c(ξ) - ζ) @ ζ = 0.1mm : z} / 'Shear area -'A_Q(ξ) = I(ξ)^2/$Area{S_1(ξ; z)^2/b(ξ; z) @ z = 0.1mm : h(ξ) - 0.1mm} / '<h4>Element stiffness matrix</h4> / 'Elastic properties for element "e" / EA(e; x) = E.e_M.e*A(x/l(e)) / EI(e; x) = E.e_M.e*I(x/l(e)) / GA_Q(e; x) = G.e_M.e*A_Q(x/l(e)) / 'Stiffness matrix for element with variable cross-section / 'Displacement due to F<sub>x</sub> = 1 in primary system -'u_F(e) = $Area{1/EA(e; x) @ x = 0m : l(e)} / 'Displacement due to F<sub>y1</sub> = 1 in primary system, with account of shear deflections -'v_F1(e) = $Area{x^2/EI(e; x) @ x = 0m : l(e)} + $Area{1/GA_Q(e; x) @ x = 0m : l(e)} / 'Rotation due to F<sub>y1</sub> = 1 in primary system -'φ_F1(e) = -$Area{x/EI(e; x) @ x = 0m : l(e)}' + 0 / 'Displacement due to M<sub>1</sub> = 1 in primary system -'v_M1(e) = φ_F1(e) / 'Rotation due to M<sub>1</sub> = 1 in primary system -'φ_M1(e) = $Area{1/EI(e; x) @ x = 0m : l(e)}' + 0 / 'Determinant -'D_1(e) = φ_M1(e)*v_F1(e) - φ_F1(e)^2 / 'Displacement due to F<sub>y2</sub> = 1 in primary system -'v_F2(e) = $Area{(l(e) - x)^2/EI(e; x) @ x = 0m : l(e)} + $Area{1/GA_Q(e; x) @ x = 0m : l(e)} / 'Rotation due to F<sub>2</sub> = 1 in primary system -'φ_F2(e) = $Area{(l(e) - x)/EI(e; x) @ x = 0m : l(e)}' + 0 / 'Displacement due to M<sub>2</sub> = 1 in primary system -'v_M2(e) = φ_F2(e) / 'Rotation due to M<sub>2</sub> = 1 in primary system -'φ_M2(e) = φ_M1(e) / 'Determinant -'D_2(e) = φ_M2(e)*v_F2(e) - φ_F2(e)^2 / '3x3 blocks of the stiffness matrix for element "e" / k_ii(e) = [D_1(e)/u_F(e)*kN*m|0; φ_M1(e)*kNm; -φ_F1(e)*kN|0; -φ_F1(e)*kN; v_F1(e)*(kN/m)]*(kN^-2/D_1(e)) / k_ij(e) = [-D_2(e)/u_F(e)*kN*m|0; -φ_M2(e)*kNm; φ_F2(e)*kN|0; (φ_F2(e) - φ_M2(e)*l(e))*kN; -(v_F2(e) - φ_F2(e)*l(e))*(kN/m)]*(kN^-2/D_2(e)) / k_ji(e) = [-D_1(e)/u_F(e)*kN*m|0; -φ_M1(e)*kNm; φ_F1(e)*kN|0; (φ_F1(e) + φ_M1(e)*l(e))*kN; -(v_F1(e) + φ_F1(e)*l(e))*(kN/m)]*(kN^-2/D_1(e)) / k_jj(e) = [D_2(e)/u_F(e)*kN*m|0; φ_M2(e)*kNm; -φ_F2(e)*kN|0; -φ_F2(e)*kN; v_F2(e)*(kN/m)]*(kN^-2/D_2(e)) / 'Full element stiffness matrix / k_E(e) = stack(augment(k_ii(e); k_ij(e)); augment(k_ji(e); k_jj(e))) / 'Stiffness matrices obtained in local coordinates / k_E(1) / k_E(2) / 'Stiffness matrices obtained in global coordinates / transp(T(1))*k_E(1)*T(1) / transp(T(2))*k_E(2)*T(2) / '<h4>Global stiffness matrix</h4> / #hide / K = symmetric(3*n_J) / 'Add element stiffness matrices / #for e = 1 : n_E / i = 3*e_J.(e; 1) - 2','j = 3*e_J.(e; 2) - 2 / t = t(e)','tT = transp(t) / add(tT*k_ii(e)*t; K; i; i) / #if j > i / add(tT*k_ij(e)*t; K; i; j) / #else / add(tT*k_ji(e)*t; K; j; i) / #end if / add(tT*k_jj(e)*t; K; j; j) / #loop / 'Add supports / #for i = 1 : n_c / j = 3*c.(i; 1) - 2 / add(vec2diag(last(row(c; i); 3)/[kN/m; kN/m; kNm]); K; j; j) / #loop / #show / K / '<h4>Element load vector</h4> / 'Load functions / 'Shear -'q_E(e; x) = -q_x.e*s(e) + q_y.e*c(e) / 'Axial -'n_E(e; x) = q_x.e*c(e) + q_y.e*s(e) / 'Functions of internal forces in primary system / 'Axial forces -'N_0(e; x) = -$Area{n_E(e; ξ) @ ξ = 0m : x} / 'Shear forces -'Q_0(e; x) = $Area{q_E(e; ξ) @ ξ = 0m : x} / 'Bending moments -'M_0(e; x) = $Area{q_E(e; ξ)*(x - ξ) @ ξ = 0m : x} / 'Reactions at element ends / 'Displacements along “x“ due to axial loads -'u_n(e) = $Area{N_0(e; x)/EA(e; x) @ x = 0m : l(e)} / 'Displacements along “y“ due to lateral loads -'v_q(e) = $Area{M_0(e; x)*x/EI(e; x) @ x = 0m : l(e)} + $Area{Q_0(e; x)/GA_Q(e; x) @ x = 0m : l(e)} / 'Rotations due to lateral loads -'φ_q(e) = -$Area{M_0(e; x)/EI(e; x) @ x = 0m : l(e)} / 'Element endpoint loads in local coordinate system / 'For joint “1”: / F_x1(e) = -u_n(e)/u_F(e) / F_y1(e) = (φ_M1(e)*v_q(e) - φ_F1(e)*φ_q(e))/D_1(e) / M_1(e) = (v_F1(e)*φ_q(e) - φ_F1(e)*v_q(e))/D_1(e) / 'For joint “2”: / F_x2(e) = -F_x1(e) - N_0(e; l(e)) / F_y2(e) = -F_y1(e) + Q_0(e; l(e)) / M_2(e) = -M_1(e) + F_y1(e)*l(e) - M_0(e; l(e)) / 'Element endpoint loads in global coordinate system / 'For joint “1”: / F′_x1(e) = F_x1(e)*c(e) - F_y1(e)*s(e) / F′_y1(e) = F_x1(e)*s(e) + F_y1(e)*c(e) / 'For joint “2”: / F′_x2(e) = F_x2(e)*c(e) - F_y2(e)*s(e) / F′_y2(e) = F_x2(e)*s(e) + F_y2(e)*c(e) / 'Element load vector / F_E(e) = [F′_x1(e); F′_y1(e); M_1(e)*m^-1; F′_x2(e); F′_y2(e); M_2(e)*m^-1]*kN^-1 / #novar / #for e = 1 : n_E / F_E(e) / #loop / #varsub / '<h4>Global load vector</h4> / #hide / F = vector(3*n_J) / #for i = 1 : n_q / e = q.(i; 1) / #for jj = 1 : 2 / j = 3*e_J.(e; jj) - 3 / F.(j + 1) = F.(j + 1) + take(3*jj - 2; F_E(e)) / F.(j + 2) = F.(j + 2) + take(3*jj - 1; F_E(e)) / F.(j + 3) = F.(j + 3) + take(3*jj; F_E(e)) / #loop / #loop / #show / F / '<h4>Results</h4> / '<p><strong>Solution of the system of equations</strong></p> / Z = clsolve(K; F) / '<p><strong>Joint displacements</strong></p> / z_J(j) = slice(Z; 3*j - 2; 3*j) / z(j) = round(z_J(j)/δz)*δz*1000*[mm; mm; 1] / #novar / #for j = 1 : n_J / z(j) / #loop / #varsub / '<p><strong>Support reactions</strong></p> / r(i) = row(c; i)','j(i) = take(1; r(i)) / R(i) = -z_J(j(i))*[m; m; 1]*last(r(i); 3) / #novar / #for i = 1 : n_c / #val / '<p>Joint <b>J'j(i)' - / #equ / '</b>'R(i)'</p> / #loop / #varsub / '<p><strong>Element end forces</strong></p> / z_E(e) = [z_J(e_J.(e; 1)); z_J(e_J.(e; 2))] / R_E(e) = col(k_E(e)*T(e)*z_E(e) - T(e)*F_E(e); 1)*[1; 1; m; 1; 1; m]*kN / #novar / #for e = 1 : n_E / R_E(e) / #loop / #varsub / '<p><strong>Element internal forces</strong></p> / N(e; x) = -take(1; R_E(e)) + N_0(e; x) / Q(e; x) = take(2; R_E(e)) + Q_0(e; x) / M(e; x) = -take(3; R_E(e)) + take(2; R_E(e))*x + M_0(e; x) / #hide / w = max(x_J) / h = max(y_J) / W = 240 / H = h*W/w / k = W/w / #def red_style$ = style = "stroke:red; stroke-width:1; fill:red" / #deg / #for i = 1 : 3 / #hide / R(e; x) = take(i; N(e; x); Q(e; x); M(e; x)) / sgn = take(i; 1; 1; -1) / tol = 0.01*take(i; kN; kN; kNm) / R_max = $Sup{$Sup{R(e; x) @ x = 0m : l(e)} @ e = 1 : n_E} / R_min = $Sup{abs($Inf{R(e; x) @ x = 0m : l(e)}) @ e = 1 : n_E} / k_R = sgn*1m*k/max(R_min; R_max) / #show / #if i ≡ 1 / '<p><strong>Axial forces diagram, kN</strong></p> / #else if i ≡ 2 / '<p><strong>Shear forces diagram, kN</strong></p> / #else / '<p><strong>Bending moments diagram, kNm</strong></p> / #end if / #val / svg$ / '<use href="#frame"/> / #for e = 1 : n_E / #hide / x1 = x_1(e)*k / y1 = (h - y_1(e))*k / x2 = x_2(e)*k / y2 = (h - y_2(e))*k / c_e = c(e) / s_e = s(e) / l_e = l(e) / st = l_e/10 / xd2 = x1 / yd2 = y1 / #show / #for j = 0 : 10 / #hide / xd1 = xd2 / yd1 = yd2 / x = j*st*k / v = R(e; j*st) / y = v*k_R / xd2 = x1 + x*c_e - y*s_e / yd2 = y1 - x*s_e - y*c_e / α = 90 + atan2(c_e; s_e) / #if α ≥ 135 / α = α - 180 / #end if / #if α < -45 / α = α + 180 / #else if α < 0 / α = 360 + α / #end if / d = -15*sign(v*sgn) / #show / line$(xd1; yd1; xd2; yd2; red_style$) / #if (j ≡ 0 ∨ j ≡ 10) ∧ abs(v) > tol / text$(xd2 + s_e*d; yd2 + d*c_e; α; 'v') / #end if / line$(xd1; yd1; xd2; yd2; red_style$) / #loop / #hide / xd1 = x2 / yd1 = y2 / #show / line$(xd1; yd1; xd2; yd2; red_style$) / #loop / '</svg> / #loop / #equ / '<p><strong>Deformed shape</strong></p> / 'Shape function in relative coordinates ξ = x/l (approximate) / Φ_1(e; ξ) = 1 - 3*ξ^2 + 2*ξ^3 / Φ_2(e; ξ) = ξ*l(e)*m^-1*(1 - 2*ξ + ξ^2) / Φ_3(e; ξ) = ξ^2*(3 - 2*ξ) / Φ_4(e; ξ) = ξ^2*l(e)*m^-1*(-1 + ξ) / 'Element endpoint displacements and rotations / z_E,loc(e) = T(e)*z_E(e) / u_1(e) = take(1; z_E,loc(e))','v_1(e) = take(2; z_E,loc(e))','φ_1(e) = take(3; z_E,loc(e)) / u_2(e) = take(4; z_E,loc(e))','v_2(e) = take(5; z_E,loc(e))','φ_2(e) = take(6; z_E,loc(e)) / 'Displacement functions / u(e; ξ) = u_1(e)*(1 - ξ) + u_2(e)*ξ / v(e; ξ) = v_1(e)*Φ_1(e; ξ) + φ_1(e)*Φ_2(e; ξ) + v_2(e)*Φ_3(e; ξ) + φ_2(e)*Φ_4(e; ξ) / 'Deformed shape, mm / #val / #hide / tol = 0.00001 / k_R = 800 / #show / svg$ / '<use href="#frame" style="opacity:0.4;"/> / #for e = 1 : n_E / #hide / x1 = x_1(e)*k / y1 = (h - y_1(e))*k / x2 = x_2(e)*k / y2 = (h - y_2(e))*k / c_e = c(e) / s_e = s(e) / l_e = l(e) / u = u(e; 0) / v = v(e; 0) / x = u*k_R / y = v*k_R / xd2 = x1 + x*c_e - y*s_e / yd2 = y1 - x*s_e - y*c_e / #show / #for j = 0 : 10 / #hide / xd1 = xd2 / yd1 = yd2 / ξ = j/10 / u = u(e; ξ) / v = v(e; ξ) / x = ξ*l_e*k + u*k_R / y = v*k_R / xd2 = x1 + x*c_e - y*s_e / yd2 = y1 - x*s_e - y*c_e / d = -15*sign(v) / #show / line$(xd1; yd1; xd2; yd2; red_style$) / #loop / #loop / #for j = 1 : n_J / #hide / z_J = z_J(j) / u = z_J.1 / v = z_J.2 / x = x_J.j*k + u*k_R / y = (h - y_J.j)*k - v*k_R / dx = 15*sign(u) / dy = -15*sign(v) / #show / #if abs(u) > tol / texth$(x + dx; y; 'u*1000') / #end if / #if abs(v) > tol / textv$(x; y + dy; 'v*1000') / #end if / #loop / '</svg> / #equ

# Output
Analysis of plane frames with variable cross-sections
Joint coordinates / J1 J2 J3 J4 J5 / {widevec {x}} rsub {J} = left [0 "m " 0 "m " 8 "m " 16 "m " 16 "m" right ] / {widevec {y}} rsub {J} = left [0 "m " 8 "m " 10 "m " 8 "m " 0 "m" right ] / {n} rsub {J} = bold "len" left ({widevec {x}} rsub {J} right ) =5	Elements / e_J^T = left [matrix {1 # 3 # 3 # 5 ## 2 # 2 # 4 # 4} right ] / {n} rsub {E} = bold {"n"} rsub {rows} left ({e} rsub {J} right ) =4

Element endpoint coordinates
{x} rsub {1} left (e right ) = {{widevec {x}} rsub {J}} rsub {. {{e} rsub {J}} rsub {. e ,1}} , {y} rsub {1} left (e right ) = {{widevec {y}} rsub {J}} rsub {. {{e} rsub {J}} rsub {. e ,1}} ,	{x} rsub {2} left (e right ) = {{widevec {x}} rsub {J}} rsub {. {{e} rsub {J}} rsub {. e ,2}} , {y} rsub {2} left (e right ) = {{widevec {y}} rsub {J}} rsub {. {{e} rsub {J}} rsub {. e ,2}}
Element length- l left (e right ) = sqrt {{left ({x} rsub {2} left (e right ) - {x} rsub {1} left (e right ) right )} ^ {2} + {left ({y} rsub {2} left (e right ) - {y} rsub {1} left (e right ) right )} ^ {2}}
Element directions - c left (e right ) = {{x} rsub {2} left (e right ) - {x} rsub {1} left (e right )} over {l left (e right )} , s left (e right ) = {{y} rsub {2} left (e right ) - {y} rsub {1} left (e right )} over {l left (e right )}
Transformation matrix
Diagonal 3x3 block - t(e) = left [c(e)"; "s(e)"; "0"| -"s(e)"; "c(e)"; "0"| "0"; "0"; "1 right ]
Generation of the full transformation matrix
T(e) = bold "add" left (t(e)"; " bold "add" left (t(e) "; " bold "matrix"(6"; "6)"; "1"; "1 right )"; "4"; "4 right )

Supports / J cx cy cr / c = left [matrix {1 # {10} ^ {20} "kN" / "m" # {10} ^ {20} "kN" / "m" # 0 "kNm" ## 5 # {10} ^ {20} "kN" / "m" # {10} ^ {20} "kN" / "m" # {10} ^ {20} "kNm"} right ] / {n} rsub {c} = {"n"} rsub {rows} left (c right ) =2	Loads / е qx qy / q = left [matrix {1 # 10 "kN" / "m" # 0 "kN" / "m" ## 2 # 0 "kN" / "m" # -20 "kN" / "m" ## 3 # 0 "kN" / "m" # -10 "kN" / "m"} right ]

Load values on elements
   E1	E2	E3	E4
{widevec {q}} rsub {x} = left [10 "kN/m " 0 "kN/m " 0 "kN/m " 0 "kN/m" right ]
{widevec {q}} rsub {y} = left [0 "kN/m -"20 "kN/m -"10 "kN" / "m " 0 "kN/m" right ]
Scheme of the structure

Materials
Modules of elasticity -	widevec {E} = left [45 "GPa " 35 "GPa" right ]
Poisson coefficients -	widevec {ν} = left [0.2" "0.2 right ]
Shear modules -	widevec {G} = {widevec {E}} over {2· left (1+ widevec {ν} right )} = left [18.75 "GPa " 14.58 "GPa" right ]
Assignment on elements -	{widevec {e}} rsub {M} = [matrix{1 # 2 # 2 # 1}]
Cross-sections
Section S1 - {b} rsub {1} =300 "mm" , {h} rsub {1} =300 "mm"
Section S2 - {b} rsub {2} =300 "mm" , {h} rsub {2} =900 "mm"
General representation
Width - b left (ξ"; "z right ) = {b} rsub {1} + left ({b} rsub {2} - {b} rsub {1} right ) · ξ
Height - h left (ξ right ) = {h} rsub {1} + left ({h} rsub {2} - {h} rsub {1} right ) · ξ
Cross section properties
Area -	A(ξ) = int from {0 "mm"} to {h(ξ)} {b(ξ"; "z) nospace{"d"z}}
First moment of area -	S(ξ) = int from {0 "mm"} to {h(ξ)} {b left (ξ "; "z right ) · z nospace{"d"z}}
Centroid -	{z} rsub {c} left (ξ right ) = {S left (ξ right )} over {A left (ξ right )}
Second moment of area -	I(ξ) = int from {0 "mm"} to {h(ξ)} {b(ξ"; "z) · {left (z - z_c(ξ) right )} ^ 2 nospace{"d"z}}
First moment of area bellow z -	S_1(ξ"; "z) = int from {0"mm"} to z {b(ξ"; "ζ) · left (z_c(ξ) - ζ right) nospace{"d"ζ}}
Shear area -	A_Q(ξ) = {I(ξ)^2} over {int from {0"mm"} to {h(ξ)} {{{S_1(ξ"; "z)}^2} over {b(ξ"; "z)} nospace{"d"z}}}
Element stiffness matrix
Elastic properties for element "e"
EA(e"; "x) = {widevec {E}} rsub {{{widevec {e}} rsub {M}} rsub {.e}} · A left (x over {l(e)} right ) , EI(e"; "x) = {widevec {E}} rsub {{{widevec {e}} rsub {M}} rsub {.e}} · I left (x over {l(e)} right ) , GA_Q(e"; "x) = {widevec {G}} rsub {{{widevec {e}} rsub {M}} rsub {.e}} · A_Q left ({x} over {l(e)} right )

Stiffness matrix for element with variable cross-section
Displacement due to Fx = 1 in primary system -	u_F(e) = int from {0"m"} to {l(e)} {1 over {EA(e"; "x)} nospace{"d"x}}
Displacement due to Fy1 = 1 in primary system, with account for shear deflections - v_nospace{F1}(e) = int from {0"m"} to {l(e)} {{x^2} over {EI(e"; "x)} nospace{"d"x}} + int from {0"m"} to {l(e)} {1 over {GA_Q(e"; "x)} nospace{"d"x}}
Rotation due to Fy1 = 1 in primary system -	φ_nospace{F1}(e) = - left (int from {0"m"} to {l(e)} {x over {EI(e"; "x)} nospace{"d"x}} right )
Displacement due to M1 = 1 in primary system -	v_nospace{M1}(e) = φ_nospace{F1}(e)
Rotation due to M1 = 1 in primary system -	φ_nospace{M1}(e) = int from {0"m"} to {l(e)} {1 over {EI(e"; "x)} nospace{"d"x}}
Determinant -	D_1(e) = φ_nospace{M1}(e) · v_nospace{F1}(e) - {φ_nospace{F1}(e)}^2
Displacement due to Fy2 = 1 in primary system - v_nospace{F2}(e) = int from {0"m"} to {l(e)} {{left (l(e) - x right )^2} over {EI(e"; "x)} nospace{"d"x}} + int from {0"m"} to {l(e)} {1 over {GA_Q(e"; "x)} nospace{"d"x}}
Rotation due to Fy2 = 1 in primary system -	φ_nospace{F2}(e) = int from {0"m"} to {l(e)} {{l(e) - x} over {EI(e"; "x)} nospace{"d"x}}
Displacement due to M2 = 1 in primary system -	v_nospace{M2}(e) = φ_nospace{F2}(e)
Rotation due to M2 = 1 in primary system -	φ_nospace{M2}(e) = φ_nospace{M1}(e)
Determinant -	{D} rsub {2} left (e right ) = {φ} rsub {M 2} left (e right ) · {v} rsub {F 2} left (e right ) - {{φ} rsub {F 2} left (e right )} ^ {2}
3x3 blocks of the stiffness matrix for element "e"
k_ii(e) = left [{D_1(e)} over {u_F(e)}·kNm "|" 0"; " φ_nospace{M1}(e)·kNm"; -"φ_nospace{F1}(e)·kN "|" 0"; -"φ_nospace{F1}(e)·kN"; "v_nospace{F1}(e)·{kN} over {m} right ] · {kN^{"-"2}} over {D_1(e)}
k_ij(e) = left ["-"{D_2(e)} over {u_F(e)} · kNm "|" 0"; -"φ_nospace{M2}(e) · kNm"; "φ_nospace{F2}(e) · kN "|" 0"; "left (φ_nospace{F2}(e) - φ_nospace{M2}(e) · l(e) right )·kN"; -"left (v_nospace{F2}(e) - φ_nospace{F2}(e) · l(e) right ) · {kN} over {m} right ] · {{kN} ^ {"-"2}} over {{D} rsub {2}(e)}
k_ji(e) = left ["-"{D_1(e)} over {u_F(e)}·kNm "|" 0"; -"φ_nospace{M1}(e) · kNm"; "φ_nospace{F1}(e)·kN "|" 0"; "left (φ_nospace{F1}(e) + φ_nospace{M1}(e)·l(e) right ) · kN"; -"left (v_nospace{F1}(e) + φ_nospace{F1}(e)·l(e) right )·kN over m right ]·{kN^{"-"2}} over {D_1(e)}
k_jj(e) = left [{{D_2}(e)} over {{u_F}(e)}·kNm "|" 0"; "φ_nospace{M2}(e)·kNm"; -" φ_nospace{F2}(e)·kN "|" 0"; -"φ_nospace{F2}(e)·kN"; "v_nospace{F2}(e)·{kN} over {m} right ] · {kN^{"-"2}} over {D_2(e)}
Full element stiffness matrix
k_E(e) = bold "stack" left (bold "augment" left (k_ii(e)"; "k_ij(e) right )"; "bold "augment" left (k_ji(e)"; "k_jj(e) right ) right )
Stiffness matrices obtained in local coordinates
{k} rsub {E} left (1 right ) = left [matrix {921617 # 0 # 0 # "-"921617 # 0 # 0 ## 0 # 4741.71 # 9483.42 # 0 # "-"4741.71 # 28450.3 ## 0 # 9483.42 # 36052.8 # 0 # "-"9483.42 # 39814.6 ## "-"921617 # 0 # 0 # 921617 # 0 # 0 ## 0 # "-"4741.71 # "-"9483.42 # 0 # 4741.71 # "-"28450.3 ## 0 # 28450.3 # 39814.6 # 0 # "-"28450.3 # 187788} right ]
{k} rsub {E} left (2 right ) = left [matrix {695411 # 0 # 0 # "-"695411 # 0 # 0 ## 0 # 3370.35 # 6948.16 # 0 # "-"3370.35 # 20844.5 ## 0 # 6948.16 # 27216.3 # 0 # "-"6948.16 # 30079.7 ## "-"695411 # 0 # 0 # 695411 # 0 # 0 ## 0 # "-"3370.35 # -6948.16 # 0 # 3370.35 # "-"20844.5 ## 0 # 20844.5 # 30079.7 # 0 # "-"20844.5 # 141808} right ]
Stiffness matrices obtained in global coordinates
bold "transp" left (T left (1 right ) right ) · {k} rsub {E} left (1 right ) · T left (1 right ) = left [matrix {4741.71 # 0 # "-"9483.42 # "-"4741.71 # 0 # "-"28450.3 ## 0 # 921617 # 0 # 0 # "-"921617 # 0 ## "-"9483.42 # 0 # 36052.8 # 9483.42 # 0 # 39814.6 ## "-"4741.71 # 0 # 9483.42 # 4741.71 # 0 # 28450.3 ## 0 # "-"921617 # 0 # 0 # 921617 # 0 ## "-"28450.3 # 0 # 39814.6 # 28450.3 # 0 # 187788} right ]
bold "transp" left (T left (2 right ) right ) · {k} rsub {E} left (2 right ) · T left (2 right ) = left [matrix {654703 # 162833 # 1685.18 # "-"654703 # "-"162833 # 5055.53 ## 162833 # 44078.6 # "-"6740.7 # "-"162833 # "-"44078.6 # "-"20222.1 ## 1685.18 # "-"6740.7 # 27216.3 # "-"1685.18 # 6740.7 # 30079.7 ## "-"654703 # "-"162833 # "-"1685.18 # 654703 # 162833 # "-"5055.53 ## "-"162833 # "-"44078.6 # 6740.7 # 162833 # 44078.6 # 20222.1 ## 5055.53 # "-"20222.1 # 30079.7 # "-"5055.53 # 20222.1 # 141808} right ]
Global stiffness matrix
K = left [matrix {{10} ^ {20} # 0 # "-"9483.42 # "-"4741.71 # 0 # "-"28450.3 # 0 # 0 # 0 # 0 # 0 # 0 # 0 # 0 # 0 ## 0 # {10} ^ {20} # 0 # 0 # "-"921617 # 0 # 0 # 0 # 0 # 0 # 0 # 0 # 0 # 0 # 0 ## "-"9483.42 # 0 # 36052.8 # 9483.42 # 0 # 39814.6 # 0 # 0 # 0 # 0 # 0 # 0 # 0 # 0 # 0 ## "-"4741.71 # 0 # 9483.42 # 659445 # 162833 # 23394.7 # "-"654703 # "-"162833 # "-"1685.18 # 0 # 0 # 0 # 0 # 0 # 0 ## 0 # "-"921617 # 0 # 162833 # 965696 # 20222.1 # "-"162833 # "-"44078.6 # 6740.7 # 0 # 0 # 0 # 0 # 0 # 0 ## "-"28450.3 # 0 # 39814.6 # 23394.7 # 20222.1 # 329596 # 5055.53 # "-"20222.1 # 30079.7 # 0 # 0 # 0 # 0 # 0 # 0 ## 0 # 0 # 0 # "-"654703 # "-"162833 # 5055.53 # 1309406 # 0 # 3370.35 # "-"654703 # 162833 # 5055.53 # 0 # 0 # 0 ## 0 # 0 # 0 # "-"162833 # "-"44078.6 # "-"20222.1 # 0 # 88157.3 # 0 # 162833 # "-"44078.6 # 20222.1 # 0 # 0 # 0 ## 0 # 0 # 0 # "-"1685.18 # 6740.7 # 30079.7 # 3370.35 # 0 # 54432.6 # "-"1685.18 # "-"6740.7 # 30079.7 # 0 # 0 # 0 ## 0 # 0 # 0 # 0 # 0 # 0 # "-"654703 # 162833 # "-"1685.18 # 659445 # "-"162833 # 23394.7 # "-"4741.71 # 0 # 9483.42 ## 0 # 0 # 0 # 0 # 0 # 0 # 162833 # "-"44078.6 # "-"6740.7 # "-"162833 # 965696 # "-"20222.1 # 0 # "-"921617 # 0 ## 0 # 0 # 0 # 0 # 0 # 0 # 5055.53 # 20222.1 # 30079.7 # 23394.7 # "-"20222.1 # 329596 # "-"28450.3 # 0 # 39814.6 ## 0 # 0 # 0 # 0 # 0 # 0 # 0 # 0 # 0 # "-"4741.71 # 0 # "-"28450.3 # {10} ^ {20} # 0 # "-"9483.42 ## 0 # 0 # 0 # 0 # 0 # 0 # 0 # 0 # 0 # 0 # "-"921617 # 0 # 0 # {10} ^ {20} # 0 ## 0 # 0 # 0 # 0 # 0 # 0 # 0 # 0 # 0 # 9483.42 # 0 # 39814.6 # "-"9483.42 # 0 # {10} ^ {20}} right ]
Element load vector
Load functions
Lateral - q_E(e"; "x) ="-"{{widevec {q}} rsub {x}} rsub {.e}·s(e) + {{widevec {q}} rsub {y}} rsub {.e}·c(e)
Axial - {n_E}(e"; "x) = {{widevec {q}} rsub {x}} rsub {.e}·c(e) + {{widevec {q}} rsub {y}} rsub {.e}·s(e)
Functions of internal forces in primary system
Axial forces - N_0(e"; "x) ="-"int from {0 "m"} to {x} {n_E(e"; "ξ) nospace{"d"ξ}}
Shear forces - Q_0(e"; "x) = int from {0"m"} to {x} {q_E(e"; "ξ) nospace{"d"ξ}}
Bending moment - M_0(e"; "x) = int from {0"m"} to {x} {q_E(e"; "ξ)·(x - ξ) nospace{"d"ξ}}
Reactions at element ends
Displacements along “x“ due to axial loads - u_n(e) = int from {0"m"} to {l(e)} {{N_0(e"; "x)} over {EA(e"; "x)} nospace{"d"x}}
Displacements along “y“ due to lateral loads - v_q(e) = int from {0"m"} to {l(e)} {{M_0(e"; "x) · x} over {EI(e"; "x)} nospace{"d"x}} + int from {0"m"} to {l(e)} {{Q_0(e"; "x)} over {GA_Q(e"; "x)} nospace{"d"x}}
Rotations due to lateral loads - φ_q(e) ="-"int from {0"m"} to {l(e)} {{M_0(e"; "x)} over {EI(e"; "x)} nospace{"d"x}}
Element endpoint loads in local coordinate system
For joint “1”: / {F}_nospace{x1} left (e right ) = "-"{{u} rsub {n} left (e right )} over {{u} rsub {F} left (e right )} F_nospace{y1}(e) = {φ_nospace{M1}(e)·v_q(e) - φ_nospace{F1}(e)·φ_q(e)} over {D_1(e)} M_1(e) = {v_nospace{F1}(e) · φ_q(e) - φ_nospace{F1}(e) · v_q(e)} over {D_1(e)}	For joint “2”: / {F} rsub {x 2} left (e right ) =- {F} rsub {x 1} left (e right ) - {N} rsub {0} left (e ; l left (e right ) right ) / {F} rsub {y 2} left (e right ) =- {F} rsub {y 1} left (e right ) + {Q} rsub {0} left (e ; l left (e right ) right ) / {M} rsub {2} left (e right ) =- {M} rsub {1} left (e right ) + {F} rsub {y 1} left (e right ) · l left (e right ) - {M} rsub {0} left (e ; l left (e right ) right )

Element endpoint loads in global coordinate system
For joint “1”: / {F'}_nospace{x1}(e) = F_nospace{x1}(e)·c(e) - F_nospace{y1}(e)·s(e) / {F'}_nospace{y1}(e) = F_nospace{x1}(e)·s(e) + F_nospace{y1}(e)·c(e)	For joint “2”: / {F'}_nospace{x2}(e) = F_nospace{x2}(e)·c(e) - F_nospace{y2}(e)·s(e) / {F'}_nospace{y2}(e) = F_nospace{x2}(e)·s(e) + F_nospace{y2}(e)·c(e)

Element load vector
F_E(e) = left [{F'}_nospace{x1}(e)"; "{F'}_nospace{y1}(e)"; "M_1(e) · m^{"-"1}"; "{F'}_nospace{x2}(e)"; "{F'}_nospace{y2}(e)"; "M_2(e)· m^{"-"1} right ]·kN^{"-"1}
F_E(1) = left [31.43" "0" -"25.11" "48.57" "0" "93.68 right ]
F_E(2) = left ["-"0.675" -"64.96" "51.75" "0.675" -"99.97" -"193.14 right ]
{F} rsub {E} left (3 right ) = left [0.338" -"32.48" -"25.88" -"0.338" -"49.98" "96.57 right ]
{F} rsub {E} left (4 right ) = left [0" "0" "0" "0" "0" "0 right ]
Global load vector
matrix{widevec {F} "=" # "["31.43 # 0 # "-"25.11 # 49.25 # "-"99.97 # "-"99.46 # "-"0.338 ## " " # "-"97.44 # 25.88 # "-"0.338 # "-"49.98 # 96.57 # 0 # 0 " " 0 "]"}
Results
Solution of the system of equations
widevec {Z} = "clsolve" left (K"; "widevec {F} right )
matrix{widevec {Z}" = ["1.06×{10}^{"-"19} # "-"1.34×{10}^{"-"18} # "-"0.00122 # 0.0112 # "-"0.000145 ## " -"0.0022 # 0.0146 # "-"0.0139 # 0.00199 # 0.0179 ## " -"0.000124 # "-"0.000536 # 6.94×{10}^{"-"19} # "-"1.14×{10}^{"-"18} # "-"1.48×{10}^{"-"18}"]"}
Joint displacements
z_J(j) = bold "slice" left (widevec {Z}"; "3·j - 2"; "3·j right )
z(j) = bold "round" left ({z_J(j)} over {δz} right )·δz·1000·["mm; mm; "1]
z(1) = left [0 "mm " 0 "mm -"1.22 right ]
z(2) = left [11.23 "mm -"0.145 "mm -"2.2 right ]
z(3) = left [14.55 "mm -"13.87 "mm "1.99 right ]
z(4) = left [17.86 "mm -"0.124 "mm -"0.536 right ]
z(5) = left [0 "mm "0 "mm "0 right ]
Support reactions
r(i) = bold "row"(c"; "i) , j(i) = bold "take" left (1"; "r(i) right )
R(i) ="-"{z_J} left (j (i) right ) · ["m; m;"1]·bold "last" left (r(i)"; "3 right )
Joint J1 - R(1) = left ["-"10.56 "kN "133.56 "kN "0 "kNm" right ]
Joint J5 - R(2) = left ["-"69.44 "kN "113.82 "kN "148.05 "kNm" right ]
Element end forces
{z} rsub {E} left (e right ) = left [{z} rsub {J} left ({{e} rsub {J}} rsub {. e ,1} right )"; "{z} rsub {J} left ({{e} rsub {J}} rsub {. e ,2} right ) right ]
R_E(e) = bold "col" left (k_E(e)·T(e)·z_E(e) - T(e)·F_E(e)"; "1 right ) · left ["1; 1; m; 1; 1; m" right ]·"kN"
R_E(1) = left [133.56"kN "10.56"kN " 1.78×{10}^{"-"14}"kNm -"133.56"kN "69.44"kN -"235.56"kNm" right ]
R_E(2) = left [59.76 "kN -"47.27"kN "34.36"kNm -"99.76"kN -"112.73"kN "235.56"kNm" right ]
R_E(3) = left [74.98"kN -"13.58"kN -"34.36"kNm -"94.98"kN "93.58"kN -"407.5"kNm" right ]
R_E(4) = left [113.82"kN "69.44"kN "148.05"kNm -"113.82"kN -"69.44"kN "407.5"kNm" right ]
Element internal forces
N(e"; "x) = bold "-take" left (1"; "R_E(e) right ) + N_0(e"; "x)
Q(e"; "x) = bold "take"(2"; "R_E(e)) + Q_0(e"; "x)
M(e"; "x) = bold "-take"(3"; "R_E(e)) + bold "take"(2"; "R_E(e))·x + M_0(e"; "x)
Axial forces diagram, kN

Shear forces diagram, kN

Bending moments diagram, kNm

Deformed shape
Shape function in relative coordinates ξ = x/l (approximate)
Φ_1(e"; "ξ) = 1 - 3·ξ^2 + 2·ξ^3 ,	Φ_2(e"; "ξ) = left (1 - 2·ξ + ξ^2 right )·ξ·{l(e)} over m
Φ_3(e"; "ξ) = (3 - 2·ξ)·ξ^2 ,	Φ_4(e"; "ξ) = ("-"1 + ξ)·ξ^2·{l(e)} over m
Element endpoint displacements and rotations
{z} rsub {E , loc} left (e right ) = T left (e right ) · {z} rsub {E} left (e right )
u_1(e) = bold "take" left (1"; "z_{E,loc}(e) right ) ,	v_1(e) = bold "take" left (2"; "z_{E,loc}(e) right ) ,	φ_1(e) = bold "take" left (3"; "z_{E,loc}(e) right )
u_2(e) = bold "take" left (4"; "z_{E,loc}(e) right ) ,	v_2(e) = bold "take" left (5"; "z_{E,loc}(e) right ) ,	φ_2(e) = bold "take" left (6"; "z_{E,loc}(e) right )
Displacement functions
x_m (e"; "ξ) = 0.5 · ξ · l ( e )
u(e"; "ξ) = u_1(e)·(1 - ξ) + u_2(e)·ξ + {n_E ( e "; "x_m (e"; "ξ)) · m} over {EA (e "; "x_m (e"; "ξ) ) }· ξ · ( 1 − ξ )
v(e"; "ξ) = v_1(e)·Φ_1(e"; "ξ) + φ_1(e)·Φ_2(e"; "ξ) + v_2(e)·Φ_3(e"; "ξ) + φ_2(e)·Φ_4(e"; "ξ)
+{{q_E (e "; "x_m (e"; "ξ)) · l ( e ) ^4} over {24 · EI ( e "; "x_m (e"; "ξ) )} · {ξ^2 · ( 1 − ξ )^ 2} over {alignc"m"} + {q_E ( e "; "x_m (e"; "ξ) ) · l ( e ) ^2} over {2 · GA_s ( e "; "x_m (e"; "ξ) ) }· {ξ · ( 1 − ξ )} over {alignc"m"}}

Deformed shape, mm

# Comparison with SAP 2000
To verify the obtained results, a SAP 2000 model is developed for the same structure. A non-prismatic finite element with three intermediate points is used. The input and output data from the analysis is listed below in both text and graphics.
Input data:
S T A T I C L O A D C A S E S
STATIC CASE SELF WT
CASE TYPE FACTOR
LOAD1 DEAD 0.0000
J O I N T D A T A
JOINT GLOBAL-X GLOBAL-Y GLOBAL-Z RESTRAINTS ANGLE-A ANGLE-B ANGLE-C
1 -8.00000 0.00000 0.00000 1 1 1 0 0 0 0.000 0.000 0.000
2 -8.00000 0.00000 8.00000 0 0 0 0 0 0 0.000 0.000 0.000
3 8.00000 0.00000 0.00000 1 1 1 1 1 1 0.000 0.000 0.000
4 8.00000 0.00000 8.00000 0 0 0 0 0 0 0.000 0.000 0.000
5 0.00000 0.00000 10.00000 0 0 0 0 0 0 0.000 0.000 0.000
F R A M E E L E M E N T D A T A
FRAME JNT-1 JNT-2 SECTION ANGLE RELEASES SEGMENTS R1 R2 FACTOR LENGTH
1 1 2 VAR1 0.000 000000 2 0.000 0.000 1.000 8.000
2 3 4 VAR1 0.000 000000 2 0.000 0.000 1.000 8.000
3 5 2 VAR2 0.000 000000 2 0.000 0.000 1.000 8.246
4 5 4 VAR2 0.000 000000 2 0.000 0.000 1.000 8.246

M A T E R I A L P R O P E R T Y D A T A
  MAT MODULUS OF POISSON'S THERMAL WEIGHT PER MASS PER
LABEL ELASTICITY RATIO COEFF UNIT VOL UNIT VOL
STEEL 199947979 0.300 1.170E-05 76.820 7.827
 CONC 45000.000 0.200 9.900E-06 0.000 0.000
OTHER 24821128.4 0.200 9.900E-06 23.562 2.401
 MAT1 45000.000 0.200 1.170E-05 0.000 0.000
 MAT2 35000.000 0.300 1.170E-05 0.000 0.000
F R A M E S E C T I O N P R O P E R T Y D A T A
SECTION MAT SECTION DEPTH FLANGE FLANGE WEB FLANGE FLANGE
LABEL LABEL TYPE WIDTH THICK THICK WIDTH THICK
        TOP TOP BOTTOM BOTTOM
VAR1
FSEC10 MAT1 0.300 0.300 0.000 0.000 0.000 0.000
FSEC11 MAT1 0.600 0.300 0.000 0.000 0.000 0.000
FSEC12 MAT1 0.900 0.300 0.000 0.000 0.000 0.000
VAR2
FSEC20 MAT2 0.300 0.300 0.000 0.000 0.000 0.000
FSEC21 MAT2 0.600 0.300 0.000 0.000 0.000 0.000
FSEC22 MAT2 0.900 0.300 0.000 0.000 0.000 0.000
F R A M E S E C T I O N P R O P E R T Y D A T A
SECTION AREA TORSIONAL MOMENTS OF INERTIA SHEAR AREAS
 LABEL INERTIA I33 I22 A2 A3
FSEC10 9.000E-02 1.141E-03 6.750E-04 6.750E-04 7.500E-02 7.500E-02
FSEC11 0.180 3.708E-03 5.400E-03 1.350E-03 0.150 0.150
FSEC12 0.270 6.401E-03 1.823E-02 2.025E-03 0.225 0.225
FSEC20 9.000E-02 1.141E-03 6.750E-04 6.750E-04 7.500E-02 7.500E-02
FSEC22 0.270 6.401E-03 1.823E-02 2.025E-03 0.225 0.225
FSEC21 0.180 3.708E-03 5.400E-03 1.350E-03 0.150 0.150
F R A M E S E C T I O N P R O P E R T Y D A T A
SECTION S ECTION MODULII PLASTIC MODULII RADII OF GYRATION
 LABEL S33 S22 Z33 Z22 R33 R22
FSEC10 4.500E-03 4.500E-03 6.750E-03 6.750E-03 8.660E-02 8.660E-02
FSEC20 4.500E-03 4.500E-03 6.750E-03 6.750E-03 8.660E-02 8.660E-02
FSEC22 4.050E-02 1.350E-02 6.075E-02 2.025E-02 0.260 8.660E-02
FSEC11 1.800E-02 9.000E-03 2.700E-02 1.350E-02 0.173 8.660E-02
FSEC21 1.800E-02 9.000E-03 2.700E-02 1.350E-02 0.173 8.660E-02
FSEC12 4.050E-02 1.350E-02 6.075E-02 2.025E-02 0.260 8.660E-02
F R A M E S P A N D I S T R I B U T E D L O A D S Load Case LOAD1
FRAME TYPE DIRECTION DISTANCE-A VALUE-A DISTANCE-B VALUE-B
    3 FORCE GLOBAL-Z 0.0000 -20.0000 1.0000 -20.0000
    4 FORCE GLOBAL-Z 0.0000 -10.0000 1.0000 -10.0000
    1 FORCE GLOBAL-X 0.0000 10.0000 1.0000 10.0000

Results:
J O I N T D I S P L A C E M E N T S
JOINT LOAD U1 U2 U3 R1 R2 R3
    1 LOAD1 0 0 0 0 1.17 0
    2 LOAD1 10.80 0 -0.15 0 2.13 0
    3 LOAD1 0 0 0 0 0 0
    4 LOAD1 17.26 0 -0.12 0 0.51 0
    5 LOAD1 14.04 0 -13.53 0 -1.87 0
J O I N T R E A C T I O N S
JOINT LOAD F1 F2 F3 M1 M2 M3
1 LOAD1 -10.6271 0.0000 133.6357 0.0000 0.0000 0.0000
3 LOAD1 -69.3729 0.0000 113.7507 0.0000 -149.2315 0.0000
F R A M E E L E M E N T F O R C E S
FRAME LOC P V2 V3 T M2 M3
1 0.00 -133.64 10.63 0.00 0.00 0.00 0.00
        4.00 -133.64 -29.37 0.00 0.00 0.00 37.49
        8.00 -133.64 -69.37 0.00 0.00 0.00 234.98
2 0.00 -113.75 69.37 0.00 0.00 0.00 149.23
        4.00 -113.75 69.37 0.00 0.00 0.00 -128.26
        8.00 -113.75 69.37 0.00 0.00 0.00 -405.75
3 0.00 -59.71 -47.18 0.00 0.00 0.00 35.66
        4.12 -79.71 32.82 0.00 0.00 0.00 65.26
        8.25 -99.71 112.82 0.00 0.00 0.00 -234.98
4 0.00 -74.89 13.53 0.00 0.00 0.00 35.66
        4.12 -84.89 53.53 0.00 0.00 0.00 -102.58
        8.25 -94.89 93.53 0.00 0.00 0.00 -405.75
Labels of joints and elements

Loads and cross sections

Support reactions

Axial forces

Shear forces

Bending moments

# Conclusions
The results obtained by the SAP 2000 software match the Calcpad solution with an accuracy of 0.5%. This is likely due to the different way the elastic properties are approximated along the element length.