® / 34-36 Peyo Yavorov blvd, / Sofia 1164, Bulgaria	tel +359 2 423 4455 / proektsoft.bg@gmail.com / https://calcpad.eu

A CALCPAD PROGRAM
FOR ANALYSIS OF PLANE FRAMES
WITH ARBITRARY CROSS-SECTIONS

─◊─◊──◊───◊────⧫────◊───◊──◊─◊─

(using the finite element method)

by

Eng. Nedelcho Ganchovsky
Table of Contents
# Introduction
This Calcpad program calculates plane frames with arbitrary sections using the finite element method. The input data is entered in text format as vectors and matrices as follows:
- joint coordinates;
- joint numbers at the ends of the elements;
- material properties;
- dimensions and types of cross-sections;
- support conditions;
- load values.
As a result, diagrams of internal forces and deflections of structural elements are obtained. The schemes are automatically generated by the program, using the SVG graphical format.

# Calcpad source code
1 / 2 / 3 / 4 / 5 / 6 / 7 / 8 / 9 / 10 / 11 / 12 / 13 / 14 / 15 / 16 / 17 / 18 / 19 / 20 / 21 / 22 / 23 / 24 / 25 / 26 / 27 / 28 / 29 / 30 / 31 / 32 / 33 / 34 / 35 / 36 / 37 / 38 / 39 / 40 / 41 / 42 / 43 / 44 / 45 / 46 / 47 / 48 / 49 / 50 / 51 / 52 / 53 / 54 / 55 / 56 / 57 / 58 / 59 / 60 / 61 / 62 / 63 / 64 / 65 / 66 / 67 / 68 / 69 / 70 / 71 / 72 / 73 / 74 / 75 / 76 / 77 / 78 / 79 / 80 / 81 / 82 / 83 / 84 / 85 / 86 / 87 / 88 / 89 / 90 / 91 / 92 / 93 / 94 / 95 / 96 / 97 / 98 / 99 / 100 / 101 / 102 / 103 / 104 / 105 / 106 / 107 / 108 / 109 / 110 / 111 / 112 / 113 / 114 / 115 / 116 / 117 / 118 / 119 / 120 / 121 / 122 / 123 / 124 / 125 / 126 / 127 / 128 / 129 / 130 / 131 / 132 / 133 / 134 / 135 / 136 / 137 / 138 / 139 / 140 / 141 / 142 / 143 / 144 / 145 / 146 / 147 / 148 / 149 / 150 / 151 / 152 / 153 / 154 / 155 / 156 / 157 / 158 / 159 / 160 / 161 / 162 / 163 / 164 / 165 / 166 / 167 / 168 / 169 / 170 / 171 / 172 / 173 / 174 / 175 / 176 / 177 / 178 / 179 / 180 / 181 / 182 / 183 / 184 / 185 / 186 / 187 / 188 / 189 / 190 / 191 / 192 / 193 / 194 / 195 / 196 / 197 / 198 / 199 / 200 / 201 / 202 / 203 / 204 / 205 / 206 / 207 / 208 / 209 / 210 / 211 / 212 / 213 / 214 / 215 / 216 / 217 / 218 / 219 / 220 / 221 / 222 / 223 / 224 / 225 / 226 / 227 / 228 / 229 / 230 / 231 / 232 / 233 / 234 / 235 / 236 / 237 / 238 / 239 / 240 / 241 / 242 / 243 / 244 / 245 / 246 / 247 / 248 / 249 / 250 / 251 / 252 / 253 / 254 / 255 / 256 / 257 / 258 / 259 / 260 / 261 / 262 / 263 / 264 / 265 / 266 / 267 / 268 / 269 / 270 / 271 / 272 / 273 / 274 / 275 / 276 / 277 / 278 / 279 / 280 / 281 / 282 / 283 / 284 / 285 / 286 / 287 / 288 / 289 / 290 / 291 / 292 / 293 / 294 / 295 / 296 / 297 / 298 / 299 / 300 / 301 / 302 / 303 / 304 / 305 / 306 / 307 / 308 / 309 / 310 / 311 / 312 / 313 / 314 / 315 / 316 / 317 / 318 / 319 / 320 / 321 / 322 / 323 / 324 / 325 / 326 / 327 / 328 / 329 / 330 / 331 / 332 / 333 / 334 / 335 / 336 / 337 / 338 / 339 / 340 / 341 / 342 / 343 / 344 / 345 / 346 / 347 / 348 / 349 / 350 / 351 / 352 / 353 / 354 / 355 / 356 / 357 / 358 / 359 / 360 / 361 / 362 / 363 / 364 / 365 / 366 / 367 / 368 / 369 / 370 / 371 / 372 / 373 / 374 / 375 / 376 / 377 / 378 / 379 / 380 / 381 / 382 / 383 / 384 / 385 / 386 / 387 / 388 / 389 / 390 / 391 / 392 / 393 / 394 / 395 / 396 / 397 / 398 / 399 / 400 / 401 / 402 / 403 / 404 / 405 / 406 / 407 / 408 / 409 / 410 / 411 / 412 / 413 / 414 / 415 / 416 / 417 / 418 / 419 / 420 / 421 / 422 / 423 / 424 / 425 / 426 / 427 / 428 / 429 / 430 / 431 / 432 / 433 / 434 / 435 / 436 / 437 / 438 / 439 / 440 / 441 / 442 / 443 / 444 / 445 / 446 / 447 / 448 / 449 / 450 / 451 / 452 / 453 / 454 / 455 / 456 / 457 / 458	#include svg_drawing.cpd / "Analysis of plane frames with arbitrary cross-sections / '<h4>Joint coordinates - xJ; yJ</h4> / #hide / #deg / δz = 10^-12 / Precision = 10^-9 / x_J = [0; 0; 8; 16; 16]*m / y_J = [0; 8; 10; 8; 0]*m / #show / x_J','y_J / n_J = len(x_J) / '<h4>Elements - [J1; J2]</h4> / #hide / e_J = [1; 2|2; 3|3; 4|4; 5] / #show / transp(e_J) / n_E = n_rows(e_J) / 'Element endpoint coordinates / x_1(e) = x_J.e_J.(e; 1)','y_1(e) = y_J.e_J.(e; 1) / x_2(e) = x_J.e_J.(e; 2)','y_2(e) = y_J.e_J.(e; 2) / 'Element length - 'l(e) = sqrt((x_2(e) - x_1(e))^2 + (y_2(e) - y_1(e))^2) / 'Element direction / c(e) = (x_2(e) - x_1(e))/l(e)','s(e) = (y_2(e) - y_1(e))/l(e) / 'Transformation matrix / 'Diagonal 3x3 block -'t(e) = [c(e); s(e); 0|-s(e); c(e); 0|0; 0; 1] / 'Generation of the full transformation matrix / T(e) = add(t(e); add(t(e); matrix(6; 6); 1; 1); 4; 4) / '<h4>Supports - [Joint; cx; cy; cr]</h4> / #hide / c = [1; 10^20kN/m; 10^20kN/m; 0kNm|5; 10^20kN/m; 10^20kN/m; 10^20kNm] / #show / c / n_c = n_rows(c) / '<h4>Loads - [Element, qx, qy]</h4> / #hide / q = [1; 10kN/m; 0kN/m|2; 0kN/m; -20kN/m|3; 0kN/m; -10kN/m] / n_q = n_rows(q) / q_x = vector(n_E)*kN/m / q_y = vector(n_E)*kN/m / $Repeat{q_x.(q.(i; 1)) = q_x.(q.(i; 1)) + q.(i; 2) @ i = 1 : n_q} / $Repeat{q_y.(q.(i; 1)) = q_y.(q.(i; 1)) + q.(i; 3) @ i = 1 : n_q} / #show / q / 'Load values on elements / q_x / q_y / '<h4>Scheme of the structure</h4> / #hide / w = max(x_J) / h = max(y_J) / W = 240 / H = h*W/w / k = W/w / #def svg$ = '<svg viewbox="'-3m*k' '-2m*k' '(w + 6m)*k' '(h + 4m)*k'" xmlns="http://www.w3.org/2000/svg" version="1.1" style="font-family: Georgia Pro; font-size:4pt; width:'W + 150'pt; height:'H + 200*H/W'pt"> / #def thin_style$ = style = "stroke:green; stroke-width:1; fill:none" / #def thick_style$ = style = "stroke:green; stroke-width:2; fill:none" / k_q = m/kN / #show / #val / svg$ / #for i = 1 : n_E / #hide / x1 = x_1(i)*k / y1 = (h - y_1(i))*k / x2 = x_2(i)*k / y2 = (h - y_2(i))*k / q_xi = q_x.i / q_yi = q_y.i / α = atan2(c(i); s(i)) / #if α ≥ 135 / α = α - 180 / #end if / #if α < -45 / α = α + 180 / #else if α < 0 / α = 360 + α / #end if / #if q_xi ≠ 0kN/m / #hide / x3 = x2 - q_xi*k_q','y3 = y2 / x4 = x1 - q_xi*k_q','y4 = y1 / x = (x3 + x4)/2 - 5*sign(q_xi) / y = (y3 + y4)/2 / #show / '<polygon points="'x1','y1' 'x2','y2' 'x3','y3' 'x4','y4'" style="stroke:magenta; stroke-width:1; stroke-opacity:0.3; fill:magenta; fill-opacity:0.1;" /> / text$(x;y;α;qx='abs(q_xi)') / #end if / #if q_yi ≠ 0kN/m / #hide / x3 = x2','y3 = y2 + q_yi*k_q / x4 = x1','y4 = y1 + q_yi*k_q / x = (x3 + x4)/2 / y = (y3 + y4)/2 + 5*sign(q_yi) / #show / '<polygon points="'x1','y1' 'x2','y2' 'x3','y3' 'x4','y4'" style="stroke:dodgerblue; stroke-width:1; stroke-opacity:0.4; fill:dodgerblue; fill-opacity:0.15;" /> / text$(x;y;α;qy='abs(q_yi)') / #end if / #show / line$(x1; y1; x2; y2; main_style$) / #loop / '<g id="frame"> / #for i = 1 : n_E / #hide / x1 = x_1(i)*k / y1 = (h - y_1(i))*k / x2 = x_2(i)*k / y2 = (h - y_2(i))*k / #show / line$(x1; y1; x2; y2; main_style$) / #loop / #for i = 1 : n_c / #hide / j = c.(i; 1) / x1 = x_J.j*k / y1 = (h - y_J.j)*k / δ = w/30*k*sign(x1 - w/2*k) / x2 = x1 - δ / y2 = y1 - abs(δ) / x3 = x1 + δ / y3 = y1 + abs(δ) / #show / #if c.(i; 2) ≠ 0kN/m / #if c.(i; 3) ≠ 0kN/m / #if c.(i; 4) ≠ 0kNm / line$(x1; y1; x1; y3; thin_style$) / line$(x2; y3; x3; y3; thick_style$) / #else / line$(x2; y3; x3; y3; thick_style$) / line$(x2; y3; x1; y1; thin_style$) / line$(x3; y3; x1; y1; thin_style$) / #end if / #else / #if c.(i; 4) ≠ 0kNm / line$(x1; y1; x2; y1; thin_style$) / line$(x2; y2; x2; y3; thick_style$) / line$(x2 - δ/2; y2; x2 - δ/2; y3; thick_style$) / #else / line$(x2; y2; x1; y1; thin_style$) / line$(x2; y3; x1; y1; thin_style$) / line$(x2; y2; x2; y3; thin_style$) / line$(x2 - δ/2; y2; x2 - δ/2; y3; thick_style$) / #end if / #end if / #else / #if c.(i; 3) ≠ 0kN/m / #if c.(i; 4) ≠ 0kNm / line$(x1; y1; x1; y3; thin_style$) / line$(x2; y3; x3; y3; thick_style$) / line$(x2; y3 + abs(δ)/2; x3; y3 + abs(δ)/2; thick_style$) / #else / line$(x2; y3; x3; y3; thin_style$) / line$(x2; y3; x1; y1; thin_style$) / line$(x3; y3; x1; y1; thin_style$) / line$(x2; y3 + abs(δ)/2; x3; y3 + abs(δ)/2; thick_style$) / #end if / #else / line$(x2; y2; x3; y3; thick_style$) / #end if / #end if / #loop / '</g> / #for i = 1 : n_E / #hide / x = (x_1(i) + x_2(i))*k/2 / y = (h - (y_1(i) + y_2(i))/2)*k / #show / texth$(x + 0.8m*sign(W/2 - x)*k; y + 0.6m*k; e'i') / #loop / #for i = 1 : n_J / point$(x_J.i*k; (h - y_J.i)*k; point_style$) / texth$((x_J.i - 0.7m*sign(w/2 - x_J.i))*k; (h - y_J.i - 0.4m)*k; J'i') / #loop / dimv$((w + 2m)*k; (h - y_J.4)*k; h*k; 'y_J.4') / dimv$((w + 2m)*k; 0; (h - y_J.4)*k; 'h - y_J.4') / dimh$(0; w*k; (h + 1.5m)*k; 'w') / '</svg> / #equ / '<h4>Materials</h4> / 'Modules of elasticity -'E = [45; 35]*GPa / 'Poisson coefficients -'ν = [0.2; 0.2] / 'Shear modules -'G = E/(2*(1 + ν)) / 'Assignment on elements -'e_M = [1; 2; 2; 1] / '<h4>Cross-sections</h4> / #hide / b = vector(2)','h = vector(2) / #show / 'Section S1 -'h.1 = 500mm'- circular - 'b_C(z) = 2*sqrt((h.1/2)^2 - (z - h.1/2)^2) / 'Section S2 -'b.2 = 250mm','h.2 = 700mm'- rectangular -'b_R(z) = b.2 / 'General representation -'b(z; s) = take(s; b_C(z); b_R(z)) / '<h4>Cross section properties</h4> / 'Equations / 'Area -'A(s) = $Integral{b(z; s) @ z = 0mm : h.s} / 'First moment of area -'S(s) = $Integral{b(z; s)*z @ z = 0mm : h.s}|cm^3 / 'Centroid -'z_c(s) = S(s)/A(s)|mm / 'Second moment of area -'I(s) = $Integral{b(z; s)*(z - z_c(s))^2 @ z = 0mm : h.s} / 'First moment of area below z -'S_1(z; s) = $Integral{b(ζ; s)*(z_c(s) - ζ) @ ζ = 0mm : z} / 'Shear area -'A_s(s) = I(s)^2/$Integral{S_1(z; s)^2/b(z; s) @ z = 0mm : h.s} / 'Calculated results / 'Centroids -'z_c = [z_c(1); z_c(2)] / 'Areas -'A = [A(1); A(2)] / 'Shear areas -'A_s = [A_s(1); A_s(2)] / 'Second moments of area -'I = [I(1); I(2)] / 'Assignment on elements -'e_S = [1; 2; 2; 1] / '<h4>Element stiffness matrix</h4> / 'Elastic properties for element "e" / EA(e) = E.e_M.e*A.e_S.e / EI(e) = E.e_M.e*I.e_S.e / GA_s(e) = G.e_M.e*A_s.e_S.e / k_s(e) = 12*EI(e)/(GA_s(e)*l(e)^2) / α(e) = EA(e)/l(e)','β(e) = EI(e)/(l(e)^3*(1 + k_s(e))) / 'Stiffness matrix coefficients for element "e" / k_11(e) = α(e)*(m/kN)','k_22(e) = 12*β(e)*(m/kN)','k_23(e) = 6*β(e)*l(e)*(1/kN) / k_33(e) = (4 + k_s(e))*β(e)*l(e)^2*(1/kNm) / k_36(e) = (2 - k_s(e))*β(e)*l(e)^2*(1/kNm) / 'Assembling the 3x3 stiffness matrix blocks for element "e" / k_ii(e) = [k_11(e)|0; k_22(e); k_23(e)|0; k_23(e); k_33(e)] / k_ij(e) = [-k_11(e)|0; -k_22(e); k_23(e)|0; -k_23(e); k_36(e)] / k_ji(e) = transp(k_ij(e)) / k_jj(e) = [k_11(e)|0; k_22(e); -k_23(e)|0; -k_23(e); k_33(e)] / 'Full 6x6 element stiffness matrix / k_E(e) = stack(augment(k_ii(e); k_ij(e)); augment(k_ji(e); k_jj(e))) / 'Stiffness matrices obtained in local coordinates / k_E(1) / k_E(2) / 'Stiffness matrices obtained in global coordinates / transp(T(1))*k_E(1)*T(1) / transp(T(2))*k_E(2)*T(2) / '<h4>Global stiffness matrix</h4> / #hide / K = symmetric(3*n_J) / 'Add element stiffness matrices / #for e = 1 : n_E / i = 3*e_J.(e; 1) - 2','j = 3*e_J.(e; 2) - 2 / t = t(e)','tT = transp(t) / add(tT*k_ii(e)*t; K; i; i) / #if j > i / add(tT*k_ij(e)*t; K; i; j) / #else / add(tT*k_ji(e)*t; K; j; i) / #end if / add(tT*k_jj(e)*t; K; j; j) / #loop / 'Add supports / #for i = 1 : n_c / j = 3*c.(i; 1) - 2 / add(vec2diag(last(row(c; i); 3)/[kN/m; kN/m; kNm]); K; j; j) / #loop / #show / K / '<h4>Element load vector</h4> / 'Lateral load in local CS -'q_E(e) = -q_x.e*s(e) + q_y.e*c(e) / 'Axial load in local CS -'n_E(e) = q_x.e*c(e) + q_y.e*s(e) / 'Equivalent loads at element endpoints / F_Ex(e) = q_x.e*l(e)/2*(1/kN)','F_Ey(e) = q_y.e*l(e)/2*(1/kN) / M_E(e) = q_E(e)*l(e)^2/12*(1/kNm) / 'Load vector -'F_E(e) = [F_Ex(e); F_Ey(e); M_E(e); F_Ex(e); F_Ey(e); -M_E(e)] / #novar / 'Results for elements / #for e = 1 : n_E / 'Element Е'e' -'F_E(e) / #loop / #varsub / '<h4>Global load vector</h4> / #hide / F = vector(3*n_J) / #for i = 1 : n_q / e = q.(i; 1) / #for jj = 1 : 2 / j = 3*e_J.(e; jj) - 3 / F.(j + 1) = F.(j + 1) + take(3*jj - 2; F_E(e)) / F.(j + 2) = F.(j + 2) + take(3*jj - 1; F_E(e)) / F.(j + 3) = F.(j + 3) + take(3*jj; F_E(e)) / #loop / #loop / #show / F / '<h4>Results</h4> / '<p><strong>Solution of the system of equations by Cholesky decomposition </strong></p> / Z = clsolve(K; F) / '<p><strong>Joint displacements</strong></p> / z_J(j) = slice(Z; 3*j - 2; 3*j) / z(j) = round(z_J(j)/δz)*δz*1000*[mm; mm; 1] / #novar / #for j = 1 : n_J / z(j) / #loop / #varsub / '<p><strong>Support reactions</strong></p> / r(i) = row(c; i)','j(i) = take(1; r(i)) / R(i) = -z_J(j(i))*[m; m; 1]*last(r(i); 3) / #novar / #for i = 1 : n_c / #val / '<p>Joint <b>J'j(i)' - / #equ / '</b>'R(i)'</p> / #loop / #varsub / '<p><strong>Element end forces</strong></p> / z_E(e) = [z_J(e_J.(e; 1)); z_J(e_J.(e; 2))] / R_E(e) = col(k_E(e)*T(e)*z_E(e) - T(e)*F_E(e); 1)*[1; 1; m; 1; 1; m]*kN / #novar / #for e = 1 : n_E / R_E(e) / #loop / #varsub / '<p><strong>Element internal forces</strong></p> / N(e; x) = -take(1; R_E(e)) - n_E(e)*x / Q(e; x) = take(2; R_E(e)) + q_E(e)*x / M(e; x) = -take(3; R_E(e)) + take(2; R_E(e))*x + q_E(e)*x^2/2 / #hide / w = max(x_J) / h = max(y_J) / W = 240 / H = h*W/w / k = W/w / #def red_style$ = style = "stroke:red; stroke-width:1; fill:red" / #deg / #for i = 1 : 3 / #hide / R(e; x) = take(i; N(e; x); Q(e; x); M(e; x)) / sgn = take(i; 1; 1; -1) / tol = 0.01*take(i; kN; kN; kNm) / R_max = $Sup{$Sup{R(e; x) @ x = 0m : l(e)} @ e = 1 : n_E} / R_min = $Sup{abs($Inf{R(e; x) @ x = 0m : l(e)}) @ e = 1 : n_E} / k_R = sgn*1m*k/max(R_min; R_max) / #show / #if i ≡ 1 / '<p><strong>Axial forces diagram, kN</strong></p> / #else if i ≡ 2 / '<p><strong>Shear forces diagram, kN</strong></p> / #else / '<p><strong>Bending moments diagram, kNm</strong></p> / #end if / #val / svg$ / '<use href="#frame"/> / #for e = 1 : n_E / #hide / x1 = x_1(e)*k / y1 = (h - y_1(e))*k / x2 = x_2(e)*k / y2 = (h - y_2(e))*k / c_e = c(e) / s_e = s(e) / l_e = l(e) / st = l_e/10 / xd2 = x1 / yd2 = y1 / #show / #for j = 0 : 10 / #hide / xd1 = xd2 / yd1 = yd2 / x = j*st*k / v = R(e; j*st) / y = v*k_R / xd2 = x1 + x*c_e - y*s_e / yd2 = y1 - x*s_e - y*c_e / α = 90 + atan2(c_e; s_e) / #if α ≥ 135 / α = α - 180 / #end if / #if α < -45 / α = α + 180 / #else if α < 0 / α = 360 + α / #end if / d = -15*sign(v*sgn) / #show / line$(xd1; yd1; xd2; yd2; red_style$) / #if (j ≡ 0 ∨ j ≡ 10) ∧ abs(v) > tol / text$(xd2 + s_e*d; yd2 + d*c_e; α; 'v') / #end if / line$(xd1; yd1; xd2; yd2; red_style$) / #loop / #hide / xd1 = x2 / yd1 = y2 / #show / line$(xd1; yd1; xd2; yd2; red_style$) / #loop / '</svg> / #loop / #equ / '<p><strong>Deformed shape</strong></p> / 'Shape function in relative coordinates ξ = x/l (with account to shear deflections) / Φ_1(e; ξ) = 1/(1 + k_s(e))*(1 + k_s(e) - k_s(e)*ξ - 3*ξ^2 + 2*ξ^3) / Φ_2(e; ξ) = ξ*l(e)*m^-1/(1 + k_s(e))*(1 + k_s(e)/2 - (2 + k_s(e)/2)*ξ + ξ^2) / Φ_3(e; ξ) = ξ/(1 + k_s(e))*(k_s(e) + 3*ξ - 2*ξ^2) / Φ_4(e; ξ) = ξ*l(e)*m^-1/(1 + k_s(e))*(-k_s(e)/2 - (1 - k_s(e)/2)*ξ + ξ^2) / 'Element endpoint displacements and rotations / z_E,loc(e) = T(e)*z_E(e) / u_1(e) = take(1; z_E,loc(e))','v_1(e) = take(2; z_E,loc(e))','φ_1(e) = take(3; z_E,loc(e)) / u_2(e) = take(4; z_E,loc(e))','v_2(e) = take(5; z_E,loc(e))','φ_2(e) = take(6; z_E,loc(e)) / 'Displacement functions / u(e; ξ) = u_1(e)*(1 - ξ) + u_2(e)*ξ / v(e; ξ) = v_1(e)*Φ_1(e; ξ) + φ_1(e)*Φ_2(e; ξ) + v_2(e)*Φ_3(e; ξ) + φ_2(e)*Φ_4(e; ξ) / 'Deformed shape, mm / #val / #hide / tol = 0.00001 / k_R = 1200 / #show / svg$ / '<use href="#frame" style="opacity:0.4;"/> / #for e = 1 : n_E / #hide / x1 = x_1(e)*k / y1 = (h - y_1(e))*k / x2 = x_2(e)*k / y2 = (h - y_2(e))*k / c_e = c(e) / s_e = s(e) / l_e = l(e) / u = u(e; 0) / v = v(e; 0) / x = u*k_R / y = v*k_R / xd2 = x1 + x*c_e - y*s_e / yd2 = y1 - x*s_e - y*c_e / #show / #for j = 0 : 10 / #hide / xd1 = xd2 / yd1 = yd2 / ξ = j/10 / u = u(e; ξ) / v = v(e; ξ) / x = ξ*l_e*k + u*k_R / y = v*k_R / xd2 = x1 + x*c_e - y*s_e / yd2 = y1 - x*s_e - y*c_e / d = -15*sign(v) / #show / line$(xd1; yd1; xd2; yd2; red_style$) / #loop / #loop / #for j = 1 : n_J / #hide / z_J = z_J(j) / u = z_J.1 / v = z_J.2 / x = x_J.j*k + u*k_R / y = (h - y_J.j)*k - v*k_R / dx = 15*sign(u) / dy = -15*sign(v) / #show / #if abs(u) > tol / texth$(x + dx; y; 'u*1000') / #end if / #if abs(v) > tol / textv$(x; y + dy; 'v*1000') / #end if / #loop / '</svg> / #equ

# Output
Analysis of plane frames with arbitrary cross-sections
Joint coordinates / J1 J2 J3 J4 J5 / {widevec {x}} rsub {J} = left [matrix {0"m" # 0"m" # 8"m" # 16"m" # 16"m"} right ] / {widevec {y}} rsub {J} = left [matrix{0"m" # 8"m" # 10"m" # 8"m" # 0"m"} right ] / Number of joints - {n} rsub {J} = bold "len" left ({widevec {x}} rsub {J} right ) =5	Elements / J1 J2 / e_J = left [matrix {1 # 2 ## 2 # 3 ## 3 # 4 ## 4 # 5} right ] / Number of elements - {n} rsub {E} = {bold "n"} rsub {rows} left ({e} rsub {J} right ) =4
Supports / J cx cy cr / c = left [matrix {1 # 10^20 "kN/m" # 10^20 "kN/m" # 0 "kNm" ## 5 # 10^20 "kN/m" # 10^20 "kN/m" # 10^20 "kNm"} right ] / Number of supports - {n} rsub {c} = {"n"} rsub {rows} left (c right ) =2	Loads / е qx qy / q = left [matrix {1 # 10 "kN/m" # 0 "kN/m" ## 2 # 0 "kN/m" # "-"20 "kN/m" ## 3 # 0 "kN/m" # "-"10 "kN/m"} right ] / Load values on elements / E1 E2 E3 E4 / {widevec q}_x = [matrix{10"kN/m" # 0"kN/m" # 0"kN/m" # 0"kN/m"}] / {widevec q}_y = [ matrix{0 "kN/m" # "-"20 "kN/m" # "-"10 "kN/m" # 0 "kN/m"}]

Element endpoint coordinates
{x} rsub {1} left (e right ) = {{widevec {x}} rsub {J}} rsub {. {{e} rsub {J}} rsub {. e 1}} , {y} rsub {1} left (e right ) = {{widevec {y}} rsub {J}} rsub {. {{e} rsub {J}} rsub {. e 1}} ,
{x} rsub {2} left (e right ) = {{widevec {x}} rsub {J}} rsub {. {{e} rsub {J}} rsub {. e 2}} , {y} rsub {2} left (e right ) = {{widevec {y}} rsub {J}} rsub {. {{e} rsub {J}} rsub {. e 2}}
Element length -	l left (e right ) = sqrt {{left ({x} rsub {2} left (e right ) - {x} rsub {1} left (e right ) right )} ^ {2} + {left ({y} rsub {2} left (e right ) - {y} rsub {1} left (e right ) right )} ^ {2}}
Element direction -	c left (e right ) = {{x} rsub {2} left (e right ) - {x} rsub {1} left (e right )} over {l left (e right )} , s left (e right ) = {{y} rsub {2} left (e right ) - {y} rsub {1} left (e right )} over {l left (e right )}
Transformation matrix
Diagonal 3x3 block - t(e) = left [c(e)"; "s(e)"; "0"| "-s(e)"; "c(e)"; "0 "| "0"; "0"; "1 right]
Generation of the full transformation matrix
T(e) = bold "add" left (t(e) "; " bold "add" left (t(e) "; " bold "matrix"(6"; "6)"; "1"; "1 right )"; "4"; "4 right )
Scheme of the structure

Materials
Modules of elasticity -	widevec {E} = [matrix{45"GPa" # 35"GPa"}]
Poisson coefficients -	widevec {ν} = [matrix{0.2 # 0.2}]
Shear modules -	widevec {G} = {widevec {E}} over {2·(1 + widevec {ν})} = [matrix{18.75"GPa" # 14.58"GPa"}]
Assignment on elements -	{widevec {e}} rsub {M} = [matrix{1 # 2 # 2 # 1}]
Cross-sections
Section S1 - {widevec {h}} rsub {1} =500 "mm" - circular - {b} rsub {C} left (z right ) =2· sqrt {{left ({{widevec {h}} rsub {1}} over {2} right )} ^ {2} - {left (z - {{widevec {h}} rsub {1}} over {2} right )} ^ {2}}
Section S2 - {widevec {b}} rsub {2} =250 "mm" , {widevec {h}} rsub {2} =700 "mm" - rectangular - {b} rsub {R} left (z right ) = {widevec {b}} rsub {2}
General representation - b(z"; "s) = bold "take"(s"; "b_C(z)"; "b_R(z))
Cross section properties
Equations
Area - A(s) = int from {0"mm"} to {{widevec h}_s} {b(z"; "s) " d"z}
First moment of area - S(s) = int from {0"mm"} to {{widevec h}_s} {b(z"; "s)·z " d"z}
Centroid - {z} rsub {c} left (s right ) = {S left (s right )} over {A left (s right )}
Second moment of area - I(s) = int from {0"mm"} to {{widevec h}_s} {b(z"; "s) · {(z - z_c(s))}^2 " d"z}
First moment of area below z - S_1(z"; "s) = int from {0"mm"} to {z} {b(ζ"; "s) · left (z_c(s) - ζ right ) " d"ζ}
Shear area - A_s(s) = {I(s)^2} over {int from {0"mm"} to {{widevec h}_s} {{S_1(z"; "s)^2} over {b(z"; "s)}nospace{" d"z}}}
Calculated results
Centroids -	{widevec z}_c = [z_c(1)"; " z_c(2)] = [matrix{250"mm" # 350"mm"}]
Areas -	widevec {A} = [A(1)"; " A(2)] = [matrix{196350"mm"^2 # 175000"mm"^2}]
Shear areas -	{widevec A}_s = [A_s(1)"; " A_s(2)] = [matrix{176715"mm"^2 # 145833"mm"^2}]
Second moments of area -	widevec {I} = [I(1)"; " I(2)] = [matrix{3067961576"mm"^4 # 7145833333"mm"^4}]
Assignment on elements -	{widevec e}_s = [matrix{1 # 2 # 2 # 1}]
Element stiffness matrix
Elastic properties for element "e"
EA left (e right ) = {widevec {E}} rsub {{{widevec {e}} rsub {M}} rsub {. e}} · {widevec {A}} rsub {{{e} rsub {S}} rsub {. e}} EI left (e right ) = {widevec {E}} rsub {{{widevec {e}} rsub {M}} rsub {. e}} · {widevec {I}} rsub {{{e} rsub {S}} rsub {. e}} {GA} rsub {s} left (e right ) = {widevec {G}} rsub {{{widevec {e}} rsub {M}} rsub {. e}} · {{widevec {A}} rsub {s}} rsub {. {{e} rsub {S}} rsub {. e}} {k} rsub {s} left (e right ) = {12· EI left (e right )} over {{GA} rsub {s} left (e right ) · {l left (e right )} ^ {2}}
α left (e right ) = {EA left (e right )} over {l left (e right )} , β left (e right ) = {EI left (e right )} over {{l left (e right )} ^ {3} · left (1+ {k} rsub {s} left (e right ) right )}
Stiffness matrix coefficients for element "e"
{k} rsub {11} left (e right ) = α left (e right ) · "m" over "kN" , {k} rsub {22} left (e right ) =12· β left (e right ) · "m" over "kN" , {k} rsub {23} left (e right ) =6· β left (e right ) · l left (e right ) · 1 over "kN"
{k} rsub {33} left (e right ) = left (4+ {k} rsub {s} left (e right ) right ) · β left (e right ) · {l left (e right )} ^ {2} · 1 over "kNm" , {k} rsub {36} left (e right ) = left (2- {k} rsub {s} left (e right ) right ) · β left (e right ) · {l left (e right )} ^ {2} · 1 over "kNm"
Assembling the 3x3 stiffness matrix blocks for element "e"
k_ii(e) = left [{k_11}(e)"| "0"; "k_22(e)"; "k_23(e)"| "0"; "k_23(e)"; "k_33(e) right ]
k_ij(e) = left ["-"k_11(e)"| "0"; -"k_22(e)"; "k_23(e)"| "0"; -"k_23(e)"; "k_36(e) right ]
{k} rsub {ji} left (e right ) = bold "transp" left ({k} rsub {ij} left (e right ) right )
k_jj(e) = left [k_11(e)"| "0"; "k_22(e)"; -"k_23(e)"| "0"; -"k_23(e)"; "k_33(e) right ]
Full 6x6 element stiffness matrix
k_E(e) = bold "stack" left ( bold "augment" left (k_ii(e)"; "k_ij(e) right )"; "bold "augment" left (k_ji(e)"; "k_jj(e) right ) right )
Stiffness matrices obtained in local coordinates
{k} rsub {E} left (1 right ) = left [matrix {1104466 # 0 # 0 # -1104466 # 0 # 0 ## 0 # 3210.66 # 12842.6 # 0 # -3210.66 # 12842.6 ## 0 # 12842.6 # 68627.8 # 0 # -12842.6 # 34113.2 ## -1104466 # 0 # 0 # 1104466 # 0 # 0 ## 0 # -3210.66 # -12842.6 # 0 # 3210.66 # -12842.6 ## 0 # 12842.6 # 34113.2 # 0 # -12842.6 # 68627.8} right ]
{k} rsub {E} left (2 right ) = left [matrix {742765 # 0 # 0 # -742765 # 0 # 0 ## 0 # 5243.46 # 21619.3 # 0 # -5243.46 # 21619.3 ## 0 # 21619.3 # 119468 # 0 # -21619.3 # 58809.3 ## -742765 # 0 # 0 # 742765 # 0 # 0 ## 0 # -5243.46 # -21619.3 # 0 # 5243.46 # -21619.3 ## 0 # 21619.3 # 58809.3 # 0 # -21619.3 # 119468} right ]
Stiffness matrices obtained in global coordinates
bold "transp" left (T(1) right ) · k_E(1) · T(1) = left [matrix {3210.66 # 0 # "-"12842.6 # "-"3210.66 # 0 # "-"12842.6 ## 0 # 1104466 # 0 # 0 # "-"1104466 # 0 ## "-"12842.6 # 0 # 68627.8 # 12842.6 # 0 # 34113.2 ## "-"3210.66 # 0 # 12842.6 # 3210.66 # 0 # 12842.6 ## 0 # "-"1104466 # 0 # 0 # 1104466 # 0 ## "-"12842.6 # 0 # 34113.2 # 12842.6 # 0 # 68627.8} right ]
bold "transp" left (T(2) right ) · k_E(2) · T(2) = left [matrix {699382 # 173535 # "-"5243.46 # "-"699382 # "-"173535 # "-"5243.46 ## 173535 # 48627.1 # 20973.8 # "-"173535 # "-"48627.1 # 20973.8 ## "-"5243.46 # 20973.8 # 119468 # 5243.46 # "-"20973.8 # 58809.3 ## "-"699382 # "-"173535 # 5243.46 # 699382 # 173535 # 5243.46 ## "-"173535 # "-"48627.1 # "-"20973.8 # 173535 # 48627.1 # "-"20973.8 ## "-"5243.46 # 20973.8 # 58809.3 # 5243.46 # "-"20973.8 # 119468} right ]
Global stiffness matrix
It is formed by adding the 3x3 blocks of the element stiffness matrices to the 3x3 blocks in the global stiffness matrix with indices corresponding to the joint numbers at the ends of the respective elements.
K = left [matrix {10^20 # 0 # "-"12842.6 # "-"3210.66 # 0 # "-"12842.6 # 0 # 0 # 0 # 0 # 0 # 0 # 0 # 0 # 0 ## 0 # 10^20 # 0 # 0 # "-"1104466 # 0 # 0 # 0 # 0 # 0 # 0 # 0 # 0 # 0 # 0 ## "-"12842.6 # 0 # 68627.8 # 12842.6 # 0 # 34113.2 # 0 # 0 # 0 # 0 # 0 # 0 # 0 # 0 # 0 ## "-"3210.66 # 0 # 12842.6 # 702592 # 173535 # 7599.17 # "-"699382 # "-"173535 # "-"5243.46 # 0 # 0 # 0 # 0 # 0 # 0 ## 0 # "-"1104466 # 0 # 173535 # 1153093 # 20973.8 # "-"173535 # "-"48627.1 # 20973.8 # 0 # 0 # 0 # 0 # 0 # 0 ## "-"12842.6 # 0 # 34113.2 # 7599.17 # 20973.8 # 188096 # 5243.46 # "-"20973.8 # 58809.3 # 0 # 0 # 0 # 0 # 0 # 0 ## 0 # 0 # 0 # "-"699382 # "-"173535 # 5243.46 # 1398763 # 0 # 10486.9 # "-"699382 # 173535 # 5243.46 # 0 # 0 # 0 ## 0 # 0 # 0 # "-"173535 # "-"48627.1 # "-"20973.8 # 0 # 97254.2 # 0 # 173535 # "-"48627.1 # 20973.8 # 0 # 0 # 0 ## 0 # 0 # 0 # "-"5243.46 # 20973.8 # 58809.3 # 10486.9 # 0 # 238937 # "-"5243.46 # "-"20973.8 # 58809.3 # 0 # 0 # 0 ## 0 # 0 # 0 # 0 # 0 # 0 # "-"699382 # 173535 # "-"5243.46 # 702592 # "-"173535 # 7599.17 # "-"3210.66 # 0 # 12842.6 ## 0 # 0 # 0 # 0 # 0 # 0 # 173535 # "-"48627.1 # "-"20973.8 # "-"173535 # 1153093 # "-"20973.8 # 0 # "-"1104466 # 0 ## 0 # 0 # 0 # 0 # 0 # 0 # 5243.46 # 20973.8 # 58809.3 # 7599.17 # "-"20973.8 # 188096 # "-"12842.6 # 0 # 34113.2 ## 0 # 0 # 0 # 0 # 0 # 0 # 0 # 0 # 0 # "-"3210.66 # 0 # "-"12842.6 # 10^20 # 0 # "-"12842.6 ## 0 # 0 # 0 # 0 # 0 # 0 # 0 # 0 # 0 # 0 # "-"1104466 # 0 # 0 # 10^20 # 0 ## 0 # 0 # 0 # 0 # 0 # 0 # 0 # 0 # 0 # 12842.6 # 0 # 34113.2 # "-"12842.6 # 0 # 10^20} right ]

Element load vector
Lateral load in local CS - {q} rsub {E} left (e right ) =- {{widevec {q}} rsub {x}} rsub {. e} · s left (e right ) + {{widevec {q}} rsub {y}} rsub {. e} · c left (e right )
Axial load in local CS - {n} rsub {E} left (e right ) = {{widevec {q}} rsub {x}} rsub {. e} · c left (e right ) + {{widevec {q}} rsub {y}} rsub {. e} · s left (e right )
Equivalent loads at element endpoints
{F} rsub {Ex} left (e right ) = {{{widevec {q}} rsub {x}} rsub {. e} · l left (e right )} over {2} · {1} over "kN" , {F} rsub {Ey} left (e right ) = {{{widevec {q}} rsub {y}} rsub {. e} · l left (e right )} over {2} · {1} over "kN" , {M} rsub {E} left (e right ) = {{q} rsub {E} left (e right ) · {l left (e right )} ^ {2}} over {12} · {1} over "kNm"
Load vector - F_E(e) = left [F_Ex(e)"; "F_Ey(e)"; "M_E(e)"; "F_Ex(e)"; "F_Ey(e)"; -"M_E(e) right ]
Results for elements
Element Е1 - {F} rsub {E} left (1 right ) = left [matrix{40 # 0 # "-"53.33 # 40 # 0 # 53.33} right ]
Element Е2 - {F} rsub {E} left (2 right ) = left [matrix{0 # "-"82.46 # "-"109.95 # 0 # "-"82.46 # 109.95} right ]
Element Е3 - {F} rsub {E} left (3 right ) = left [matrix{0 # "-"41.23 # "-"54.97 # 0 # "-"41.23 # 54.97} right ]
Element Е4 - {F} rsub {E} left (4 right ) = left [matrix{0 # 0 # 0 # 0 # 0 # 0} right ]
Global load vector
widevec {F} = left [matrix{40 # 0 # "-"53.33 # 40 # "-"82.46 # "-"56.62 # 0 # "-"123.69 # 54.97 # 0 # "-"41.23 # 54.97 # 0 # 0 # 0} right ]
Results
Solution of the system of equations by Cholesky decomposition
widevec {Z} = bold "clsolve"(K"; "widevec F) = [1.88×10-19 -1.39×10-18 -0.000928 0.00809 -0.000126
-0.00274 0.0119 -0.0157 0.000699 0.0157 -9.84×10-5 0.000846 6.12×10-19
-1.09×10-18 -2.3×10-18 ]
Joint displacements
The displacements for each joint are extracted from the global vector:
{z} rsub {J} left (j right ) = bold "slice" left (widevec {Z}"; "3· j - 2"; "3· j right ) , z left (j right ) = bold "round" left ({{z} rsub {J} left (j right )} over {10^-12} right ) · 10^-9· left ["mm; mm; 1" right ]
Values for joints
u	v	φ·103
Joint J1 - z(1) = [matrix{0"mm " # 0"mm " # "-"0.928}]
Joint J2 - z(2) = [matrix{8.09"mm" # "-"0.126"mm" # "-"2.74}]
Joint J3 - z(3) = [matrix{11.88"mm" # "-"15.67"mm" # 0.699}]
Joint J4 - z(4) = [matrix{15.67"mm" # "-"0.0984"mm" # 0.846}]
Joint J5 - z left (5 right ) = left [matrix{0"mm" # 0"mm" # 0} right ]
Support reactions
They are determined by multiplying the joint displacements by the respective spring constants.
r(i) = bold "row"(c"; "i) , j(i) = bold "take" left (1"; "r(i) right ) , R(i) = "-"z_J left (j(i) right ) · ["m; m; 1"] · bold "last" left (r(i)"; "3 right )
Values for supports
Fx	Fy	M
Joint J1 - R(1) = [matrix{"-"18.84"kN" # 138.69"kN" # 0"kNm"}]
Joint J5 - R(2) = [matrix{"-"61.16"kN" # 108.7"kN" # 230.05"kNm"}]
Element end forces
Element endpoint displacements - {z} rsub {E} left (e right ) = left [{z} rsub {J} left ({{e} rsub {J}} rsub {. e 1} right ) ; {z} rsub {J} left ({{e} rsub {J}} rsub {. e 2} right ) right ]
Endpoint forces are determined by multiplying the element stiffness matrix by the endpoint displacements in local CS and subtracting the element load vector values in local CS.
{R} rsub {E} left (e right ) = "col" left ({k} rsub {E} left (e right ) · T left (e right ) · {z} rsub {E} left (e right ) - T left (e right ) · {F} rsub {E} left (e right ) ;1 right ) · left [1;1; m ;1;1; m right ] · kN
End forces values for different elements
Fx1	Fy1	M1	Fx2	Fy2	M2
R_E(1) = [matrix{138.69 "kN" # 18.84"kN" # "-"1.42×10^{"-"14}"kNm" # "-"138.69"kN" # 61.16"kN" # "-"169.29"kNm"}]
R_E(2) = [matrix{92.97"kN" # 119.71"kN" # 169.29"kNm" # "-"52.97"kN" # 40.29"kN" # 158.18"kNm"}]
R_E(3) = [matrix{65.7"kN" # "-"10.62"kN" # "-"158.18"kNm" # "-"85.7"kN" # 90.62"kN" # "-"259.24"kNm"}]
R_E(4) = [matrix{108.7"kN" # 61.16"kN" # 259.24"kNm" # "-"108.7"kN" # "-"61.16"kN" # 230.05"kNm"}]
Element internal forces
Axial forces - N(e"; "x) = "-"bold "take" left (1"; "R_E(e) right ) - n_E(e) · x , kN

Shear forces- Q(e"; "x) = bold "take" left (2"; "R_E(e) right ) + q_E(e) · x , kN

Bending moments- M(e"; "x) = "-" bold "take" left (3"; "R_E(e) right ) + bold "take" left (2"; "R_E(e) right ) · x + {q_E(e) · x^2} over 2 , kNm

Deformed shape
Shape function in relative coordinates ξ = x/l (with account to shear deflections)
Φ_1(e"; "ξ) = 1 over {1 + k_s(e)} · left (1 + k_s(e) - k_s(e)·ξ - 3·ξ^2 +2·ξ^3 right )
Φ_2(e"; "ξ) = {ξ · l(e)·m^{"-"1}} over {1 + k_s(e)}·left (1 + {k_s(e)} over 2 - left (2 + {k_s(e)} over 2 right ) · ξ + {ξ} ^ {2} right )
Φ_3(e"; "ξ) = ξ over {1 + k_s(e)} · left (k_s(e) + 3·ξ - 2·ξ^2 right )
Φ_4(e"; "ξ) = {ξ·l(e)·m^{"-"1}} over {1 + k_s(e)} · left ("-"{k_s(e)} over 2 - left (1 - {k_s(e)} over 2 right )·ξ + ξ^2 right )
Element endpoint displacements and rotations
z_{E,loc}(e) = T(e)·z_E(e)
u_1(e) = bold "take" left (1"; "z_{E,loc}(e) right ) , v_1(e) = bold "take" left (2"; "z_{E,loc}(e) right ) , φ_1(e) = bold "take" left (3"; "z rsub {E,loc}(e) right )
u_2(e) = bold "take" left (4"; "z_{E,loc}(e) right ) , v_2(e) = bold "take" left (5"; "z_{E,loc}(e) right ) , φ_2(e) = bold "take" left (6"; "z rsub {E,loc}(e) right )
Displacement functions
u(e"; "ξ) = u_1(e)·(1 - ξ) + u_2(e)·ξ + {n_E ( e ) · m} over {EA ( e ) }· ξ · ( 1 − ξ )
v(e"; "ξ) = v_1(e)·Φ_1(e"; "ξ) + φ_1(e)·Φ_2(e"; "ξ) + v_2(e)·Φ_3(e"; "ξ) + φ_2(e)·Φ_4(e"; "ξ)
+{{q_E ( e ) · l ( e ) ^4} over {24 · EI ( e )} · {ξ^2 · ( 1 − ξ )^ 2} over {alignc"m"} + {q_E ( e ) · l ( e ) ^2} over {2 · GA_s ( e ) }· {ξ · ( 1 − ξ )} over {alignc"m"}}
Deformed shape, mm

# Comparison with Stadyps 6.0 software
Input data
Number of joints: 5 , Number of elements: 4
Joint coordinates
№	X	Y	№	X	Y	№	X	Y	№	X	Y	№	X	Y
1	0.00	0.00	2	0.00	8.00	4	16.00	8.00	3	8.00	10.00	5	16.00	0.00

Materials
№	Е		
1	45000000	0.200	0.000012
2	35000000	0.200	0.000012

Cross-sections
Section S1 - CIRCULAR
	d [mm]	CZ [cm]	CY [cm]	A [cm2]
	500.0	25.0	25.0	1963.5
	IY [cm4]	IY [cm]	WY [cm3]	IZ [cm4]	IZ [cm]	WZ [cm3]
	306796	12.5	12271.	306796	12.5	12271.
	It [cm4]	Wt [cm3]	AqZ [cm2]	AqY [cm2]
	613592	24543.	1767.1	1767.1

Section R1 - RECTANGULAR
	b [mm]	h [mm]	CZ [cm]	CY [cm]	A [cm2]
	250.0	700.0	35.0	12.5	1750.0
	IY [cm4]	IY [cm]	WY [cm3]	IZ [cm4]	IZ [cm]	WZ [cm3]
	714583	20.2	20416.	91145.	7.2	7291.7
	It [cm4]	Wt [cm3]	AqZ [cm2]	AqY [cm2]
	282662	11767.	1458.3	1458.3

Elements
№	J1	J2	Type	Material	Section	ISZ	Winkl. Const.
1	1	2	3	1	S1	0	0.0
2	2	3	3	2	R1	0	0.0
3	3	4	3	2	R1	0	0.0
4	4	5	3	1	S1	0	0.0

Supports and springs
№	Kxm	Kym	Kz	Kxy	Kxz	Kyz	Joints
4	-1	-1	0	0	0	0	1
7	-1	-1	-1	0	0	0	5

Linearly distributed loads
№	Type	q1	q2	A	L	Elements
1	qx	10.00	10.00	0.00	0.00	1
2	qy	10.00	10.00	0.00	0.00	2, 2, 3

Results
Joint displacements
Joint	Ux	Uy	Rz	Joint	Ux	Uy	Rz
1	0.000	0.000	0.001	2	0.008	0.000	0.003
3	0.012	0.016	-0.001	4	0.016	0.000	-0.001
5	0.000	0.000	0.000

Reactions in supports
Joint	Fx	Fy	Mz	Възел	Fx	Fy	Mz
1	-18.839	-138.687	0.000	5	-61.161	-108.700	-230.046

Internal forces in elements
Element	Joint	M	N	Q	Joint	M	N	Q
1	1	0.00	-138.69	18.84	2	-169.29	-138.69	-61.16
2	2	-169.29	-92.97	119.71	3	158.18	-52.97	-40.29
3	3	158.18	-65.70	-10.62	4	-259.24	-85.70	-90.62
4	4	-259.24	-108.70	61.16	5	230.05	-108.70	61.16

Loads and support reactions, kN	Axial forces, kN

Shear forces, kN	Bending moments, kNm

The results are almost identical.